## Slide 1: Memory Hierarchy Design - Cache Memory -
Jie Zhang
jiez@pku.edu.cn
[Adapted from EE488, Myoungsoo Jung, KAIST]
Notes: 内存的层次结构
缓存内存

## Slide 2: Introduction of Cache
Sandy Bridge die shot (18.5mm2)
Source: wikichip.org
Execution Units
L1D$
L2$
L1I$
O3 Scheduling Retirement
Mem Management & Execution
Notes: Cache占了处理器芯片的很大一部分
1. 为啥需要用到缓存？

## Slide 3: Review: Major Components of a Computer
Processor
Control
Datapath
Memory
I/O Devices
Input
Output
Notes: Review: load/store instruction needs to access data from memory. Memory access latency can stall the load/store instructions.

## Slide 4: Why Do We Need the Cache Memory?
The “Memory wall": Logic vs. DRAM speed gap continues to grow
Chart: 
| VAX/1980 | PPro/1996 | 2010+
Core | 10 | 0.25 | 0.042
Memory | 6 | 80 | 1000
Clocks per instruction
Clocks per DRAM access
Notes: How to address this challenge?
Why does DRAM access time increase?

## Slide 5: Memory Hierarchy Technologies
Random Access
  “Random” is good: access time is the same for all locations
  DRAM : Dynamic Random Access Memory
    High density (1 transistor cells), low power, cheap, slow
    Dynamic: need to be “refreshed” regularly (~ every 8 ms)
  SRAM : Static Random Access Memory
    Low density (6 transistor cells), high power, expensive, fast
    Static: content will last “forever” (until power turned off)
  Size: DRAM/SRAM ­ 4 to 16
  Cycle time: DRAM/SRAM ­ 8 to 16
“Non-so-random” Access Technology
  Access time varies from operation to operation, from location to location, and from time to time (e.g., tape, Disk, CDROM, SSD)
Notes: Introduce different types of memories
Q1: What’s the meaning of random access?
Q2: DRAM/SRAM size is small?

## Slide 6: Memory Hierarchy Technologies
SRAM cell
DRAM cell
WL
BL
WL
WL
BL
BL
Notes: Q1: What’s WL and BL?
Q2: What’re P/N transistors?
Q3: Why does SRAM take more area than DRAM?
Q4: How does SRAM work?
Q5: Why does SRAM consume more power?
Q6: Why is SRAM faster than DRAM?

## Slide 7: Classical RAM Organization
R
o
w
D
e
c
o
d
e
r
row
address
data bit or word
RAM Cell
Array
word (row) line
bit (data) lines
Each intersection represents a
6-T SRAM cell or a 1-T DRAM cell
Column Selector &
I/O Circuits
column
address
One memory row holds a block of data, so the column address selects the requested bit or word from that block
Buffer
col 7
col 0
Notes: Explain how RAM organization impacts the latency

## Slide 8: Memory Hierarchy: Goals
Fact: Large memories are slow, fast memories are small
How do we create a memory that gives the illusion of being large, cheap and fast (most of the time)?
by taking advantage of locality
The Principle of locality: Programs access a relatively small portion of the address space at any instant of time.
Address Space
0
2n - 1
Probability
of reference

## Slide 9: Key Idea of Memory Hierarchy: Locality!
Temporal Locality
(Locality in Time)
Spatial Locality
(Locality in Space)
 Keep most recently accessed data items closer to the processor
 Move blocks consisting of contiguous words to the upper levels
[Insights for cache design]
i = i+1;
if (i < 20) {
z = i*i + 3*i - 2;
}
q = A[i];
The program is very likely to access the same data again and again over time
sum = 0;
for(i = 0; i < n; i++)
sum += a[i];
return sum;
The program is very likely to access data that is close together
Upper Level Memory
To Processor
From Processor
Lower Level Memory
i
j
k
…
a[i+1]
a[i]
a[i+3]
a[i+2]
i
j
k
…
a[i+1]
a[i]
a[i+3]
a[i+2]

## Slide 10: Memory Hierarchy Technologies
Caches use SRAM for speed and technology compatibility
  Low density (6 transistor cells), high power, expensive, fast
  Static: content will last “forever” (until power turned off)
Main Memory uses DRAM for size (density)
  High density (1 transistor cells), low power, cheap, slow
  Dynamic: needs to be “refreshed” regularly (~ every 8 ms)
    1% to 2% of the active cycles of the DRAM
  Addresses divided into 2 halves (row and column)
    RAS or Row Access Strobe triggering row decoder
    CAS or Column Access Strobe triggering column selector
Dout[15-0]
SRAM
2M x 16
Din[15-0]
Address
Chip select
Output enable
Write enable
16
16
21
Notes: 使用DRAM作为主存，使用SRAM作为DRAM的缓存

## Slide 11: A Typical Memory Hierarchy
By taking advantage of the principle of locality
  Can present the user with as much memory as is available in the cheapest technology
  at the speed offered by the fastest technology
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Storage)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
ITLB
DTLB
DRAM
Speed (%cycles): ½’s 1’s 10’s 100’s 1,0000’s
Size (bytes): 100’s 10K’s 100K’s M’s to G’s G’s to T’s
Cost: highest lowest
Notes: 目的：offer as much memory as possible and the fastest speed

## Slide 12: The Characteristics of Memory Hierarchy
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
L1$
Processor
4-8 bytes (word)
L2$
Main memory
Secondary Memory
8-64 bytes (block)
1 to 4 blocks
1,024+ bytes (disk sector = page)
Increasing distance from the processor
(Relative) size of the memory at each level
Managed by compiler
Managed by the cache controller HW
Managed by
OS (VM)
HW (TLB)
User (Files)
Notes: How is the hierarchy managed?

## Slide 13: Cache Behaviors
Hit: data is in some block in the upper level (Block X)
  Hit Rate: the fraction of memory accesses found in the upper level
  Hit Time: Time to access the upper level which consists of
    RAM access time + Time to determine hit/miss
Miss: data needs to be retrieved from a block in the lower level (e.g., Block Y)
  Miss Rate = 1 – (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level + Time to deliver the block to the processor
  Hit Time << Miss Penalty
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y

## Slide 14: Classification of Cache Misses (3Cs)
Write to
0x1234
Assumption: there are only 4 cachelines
: empty
: filled
Capacity Miss
 Although we assume 0x1234 can be put anywhere, cache cannot contain all data
Conflict Miss
 Multiple memory locations mapped to the same cache location
Compulsory Miss
 First access to a block, “cold” fact of life, not a whole lot you can do about it
0x1234
0x1234
0x5670
0x91B1
0x1112
Assumption: here is the location of 0x1234
0x1234
0x5670
0x91B1
0x1112
0x3113

## Slide 15: Measuring Cache Performance
Assuming cache hit costs are included as part of the normal CPU execution cycle
Read-stall cycles = reads / program x read miss rate x read miss penalty
Write-stall cycles = (write / program x write miss rate x write miss penalty) + write buffer stalls
We can simplify the cache metric like below
CPU time = Instruction Count x (CPIideal + Cyclesmemory-stall) x Clock Cycle
Average Memory Access Time (AMAT)
  = Hit time + Miss rate x Miss penalty
CPIstall

## Slide 16: Impacts of Cache Performance
Relative cache penalty increases as processor performance improves (e.g., faster clock rate and/or lower CPI)
  The memory speed is unlikely to improve as fast as processor cycle time. When calculating CPIstall, the cache miss penalty is measured in processor clock cycles needed to handle a miss
  In other words, while CPIideal decrases, CPIstall is dramatically increases
[Example]
CPUideal = 2
Penaltymiss = 100 cycle
Miss rate
I$ = 2%
D$= 4%
36% LD/ST
Instr’s
Cyclesmemory-stall =
CPIstall =
2% x 100 + 36% x 4% x 100 = 3.44
2 + 3.44 = 5.44
Case1: what if the CPIideal is reduced to 1?
Case2: what if the processor clock rate is doubled (doubling the miss penality)?
CPIstall = 1+ 3.44
= 4.44
Cyclesmemory-stall =
CPIstall =
2% x 200 + 36% x 4% x 200 = 6.88
2 + 6.88 = 8.88
3.44 / 5.44 = 63 %
3.44 / 4.44 = 77 %
3.44 / 5.44 = 63 %
6.88 / 8.88 = 77 %
The amount of execution time spending on memory stalls would increase

## Slide 17: Basic Cache Design
There are several questions about cache memory design
Cache
Memory
Data is copied in block-sized transfer units
Partitioned into “blocks”

## Slide 18: Design#1: Block Placement & Identification
Cache
Memory
Where can a block be placed in the upper level?
How is a block found if it is in the upper level?

## Slide 19: Method: Direct Mapped Cache
Byte offset: 2 bits
Index: 2 bits
Tag: 2 bits = {address size} – 2 – 2
  (address size = 6 bits)
For each item of data at the lower level, there is exactly one location in the cache where it might be – so lots of items at the lower level must share locations in the upper level
A simple example
  Block size = one word (32b, 4B)
  # of blocks = 4
  Memory address (assuming 64B size thereby 6b)
Byte offset
Size of block (Byte in the word) = 22
Number of blocks = 22
Index
Tag
Notes: Q1: Is this possible that we can change the index position?

## Slide 20: Direct Mapped Cache
A Simple Example
00
01
10
11
Cache
Tag
Data
Valid
Index
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main memory
Byte offset
Index
Tag
Q1: Does the data exist in the cache?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Q2: How do we find the data (block)?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)

## Slide 21: Direct Mapped Cache
A Simple Example
00
01
10
11
Cache
Tag
Data
Valid
Index
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main memory
Byte offset
Index
Tag

## Slide 22: Direct Mapped Cache
MIPS Direct Mapped Cache Example
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
20
Data
32
Hit
One word/block, cache size = 1 K words

## Slide 23: Direct Mapped Cache
Challenge1: High miss rate
Request sequence
0(0000) 1(0001) 2(0010) 3(0011) 4(0100) 3(0011) 4(0100) 15(1111)
00
01
10
11
Cache
Tag
Data
Valid
Index
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main memory
 Start with an empty cache, all blocks initially marked as not valid
Invalid
Miss!
Fill the cache
00
1
Mem[0]
Invalid
Miss!
Fill the cache
00
1
Mem[1]
Invalid
Miss!
Fill the cache
00
1
Mem[2]
Invalid
Miss!
Fill the cache
00
1
Mem[3]
Tag mismatch
Miss!
Fill the cache
01
1
Mem[4]
Tag match
Hit!
Miss
Miss
Miss
Miss
Miss
Hit
Hit
Miss
Tag match
Hit!
Tag mismatch
Miss!
Fill the cache
11
1
Mem[15]
8 request, 6 misses
Any better idea?
Byte offset
Index
Tag

## Slide 24: Solution: Multiword Block Direct Mapped
Key idea: larger block sizes take advantage of spatial locality
Four words per block, cache size = 1K words
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset

## Slide 25: Multiword Direct Mapped
Advantages: spatial locality
Same example w/ direct mapped
0(0000) 1(0001) 2(0010) 3(0011) 4(0100) 3(0011) 4(0100) 15(1111)
0
1
Cache
Tag
Data
Valid
Index
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main memory
 Start with an empty cache, all blocks initially marked as not valid
Miss
Hit
Miss
Hit
Miss
Hit
Hit
Miss
Data
Invalid
Miss!
Fill the cache
Byte offset
Index
Tag
Block offset
00
1
Mem[1]
Mem[0]
Tag match
Hit!
Invalid
Miss!
Fill the cache
00
1
Mem[3]
Mem[2]
Tag match
Hit!
Tag mismatch
Miss!
01
1
Mem[5]
Mem[4]
Fill the cache
Tag match
Hit!
Tag match
Hit!
11
1
Mem[15]
Mem[14]
Fill the cache
Tag mismatch
Miss!
8 request, 4 misses
Reduces 2 misses than one-word direct mapped

## Slide 26: Multiword Direct Mapped
Disadvantages of multiword
Chart: Block size (bytes)
| 8 | 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Cache size
But, miss rate goes up if the block size becomes a significant fraction of the cache size because the # of blocks that can be held in the same size cache is smaller

## Slide 27: Direct Mapped Cache
Challenge2: Ping pong effect
Request sequence
0(0000) 4(0100) 0(0000) 4(0100) 0(0000) 4(0100) 0(0000) 4(0100)
00
01
10
11
Cache
Tag
Data
Valid
Index
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main memory
Block offset
Block index
Tag
 Start with an empty cache, all blocks initially marked as not valid
Miss
Miss
Miss
Miss
Miss
Miss
Miss
Miss
Invalid
Miss!
Fill the cache
00
1
Mem[0]
Tag mismatch
Miss!
01
1
Mem[4]
Fill the cache
Tag mismatch
Miss!
00
1
Mem[0]
01
1
Mem[4]
00
1
Mem[0]
01
1
Mem[4]
00
1
Mem[0]
01
1
Mem[4]
8 request, 8 misses
Any better idea?

## Slide 28: Solution: Set-Associative Cache
Byte offset: 2 bits
Index: 1 bits
Tag: 3 bits = {address size} – 2 – 1
  (address size = 6 bits)
Key idea: divide the cache into sets each of which consists of n “ways” and allow a memory block to be mapped to any “ways”
A simple example
  Block size = one word (32b, 4B)
  # of blocks = 4, # of sets = 2
  Memory address (assume 6b)
Byte offset
Size of block (Byte in the word) = 22
Number of sets = 21
Index
Tag

## Slide 29: Set-Associative Cache
A Simple Example
Cache
Main memory
Byte offset
Index
Tag
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
Tag
Data
V
Set
1
0
1
Way
0
1
Q1: Does the data exist in the cache?
Compare the cache tag in the set to the high order 3 memory address bits to tell if the memory block is in the cache
Q2: How do we find the data (block)?
Use next 1 low order memory address bits – the set index – to determine which set (i.e., modulo the number of sets in the cache)

## Slide 30: Set-Associative Cache
A Simple Example
Same example w/ direct mapped
0(0000) 4(0100) 0(0000) 4(0100) 0(0000) 4(0100) 0(0000) 4(0100)
 Start with an empty cache, all blocks initially marked as not valid
Cache
0
Tag
Data
V
Set
1
0
1
Way
0
1
Main memory
Byte offset
Index
Tag
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Miss
Miss!
Fill the cache
000
1
Mem[0]
Miss!
Fill the cache
010
1
Mem[4]
Miss
Hit
Hit
Hit
Hit
Hit
Hit
Tag match
Hit!
Tag match
Hit!
8 request, 2 misses
Reduces 6 misses than one-word direct mapped

## Slide 31: Set-Associative Cache
MIPS Example: 4-Way SA
One word/block, Cache size = 1K words
28 = 256 sets each with four ways (each with one block)
Tag (22 bits)
Address of word:
Set index (8 bits)
Byte offset (2 bits)
Index
Data
Tag
V
0
1
.
.
255
Data
Tag
V
0
1
.
.
255
Data
Tag
V
0
1
.
.
255
Data
Tag
V
0
1
.
.
255
4x1 select
Data
Hit

## Slide 32: Set-Associative Cache
Disadvantage: expensive cost
Tag (22 bits)
Address of word:
Set index (8 bits)
Block offset (2 bits)
Index
Data
Tag
V
0
1
.
.
255
Data
Tag
V
0
1
.
.
255
Data
Tag
V
0
1
.
.
255
Data
Tag
V
0
1
.
.
255
4x1 select
Data
Hit
N comparators (N-way)
 Delay & area
4x1 select
Hit/Miss decision delay
Mux delay (set selection) before data is available
One word/block, Cache size = 1K words
28 = 256 sets each with four ways (each with one block)

## Slide 33: Set-Associative Cache
Data from Hennessy & Patterson, Computer Architecture
The choice of direct mapped or set associative depends on the cost of a miss versus the cost of implementation
Chart: Associativity
| 1-way | 2-way | 4-way | 8-way
4KB | 9.8 | 7.6 | 7.1 | 7.1
8KB | 6.8 | 4.9 | 4.4 | 4.4
16KB | 4.9 | 4.1 | 4.1 | 4.1
32KB | 4.2 | 3.8 | 3.7 | 3.7
64KB | 3.7 | 3.1 | 3 | 2.9
128KB | 2.1 | 1.9 | 1.9 | 1.9
256KB | 1.3 | 1.2 | 1.2 | 1.2
512KB | 0.8 | 0.7 | 0.6 | 0.6
Largest gains are in going from direct mapped to 2-way
Advantage: can reduce miss rate with small associativity
Notes: Unlike multi-word design, SA cache can always benefit from more ways.

## Slide 34: Range of Set Associative Caches
For a fixed size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
: Byte offset
: Block offset  selects the word in the block (multi-word support)
: Index  selects the set
: Tag  used for tag compare
Address decomposition
Increasing associativity
Decreasing associativity
Fully associative
(only one set)
- Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
- Smaller tags (determined by cache size)

## Slide 35: Revisit: Classification of Cache Misses (3Cs)
Write to
0x1234
Assumption: there are only 4 cachelines
: empty
: filled
Capacity Miss
 Although we assume 0x1234 can be put anywhere, cache cannot contain all data
Conflict Miss
 Multiple memory locations mapped to the same cache location
Compulsory Miss
 First access to a block, “cold” fact of life, not a whole lot you can do about it
0x1234
0x1234
0x5670
0x91B1
0x1112
Assumption: here is the location of 0x1234
0x1234
0x5670
0x91B1
0x1112
0x3113

## Slide 36: Design#3: Block Replacement
Cache
Memory
Evict the cacheline first!
Which block should be replaced on a miss?
Notes: What about direct map?
What about set-associative cache?

## Slide 37: Cache Replacement Policy
Static
  For direct mapped cache, there is only one choice
Random
  Replace a randomly chosen cacheline
FIFO
  Replace the oldest cacheline
LRU (Least Recently Used)
  Replace the least recently used line
NRU (Not Recently Used)
  Replace one of the lines that is not recently used
  In Itanium2, L1$, L2$ and L3$ use this policy

## Slide 38: Least-Recently Used (LRU):
For way = 2, LRU is equivalent to NMRU (Not Most Recently Used)
  Single bit per set indicated LRU/MRU
  Set/clear on each access
For way > 2, LRU is difficult / expensive
  Including timestamps? How many bits?
    Ideal implementation: find min timestamp on each eviction
  Sorted list? Re-sort on every access?
Let’s remember the order in which all N cachelines were last accessed
Key idea: evict block with longest reuse distance

## Slide 39: Practical Pseudo-LRU:
Each node records which half is older/newer
  - Cache ways are the leaves of the tree
Key idea: approximated LRU policy with a binary tree
Example: PLRU for 4-way set associative cache
Way A
Way B
Way C
Way D
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
0
0
0
Pointer indicates the older
0: left is older
1: right is older
All PLRU bits are initialized as 0

## Slide 40: Practical Pseudo-LRU:
Each node records which half is older/newer
  - Cache ways are the leaves of the tree
Update nodes on each reference
Key idea: approximated LRU policy with a binary tree
Example: PLRU for 4-way set associative cache
  Update order: way A  way B  way C  way D
Way A
Way B
Way C
Way D
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
0
0
0
Way A
1
Way CD is older than Way AB
Way B is older than Way A
1

## Slide 41: Practical Pseudo-LRU:
Each node records which half is older/newer
  - Cache ways are the leaves of the tree
Update nodes on each reference
Key idea: approximated LRU policy with a binary tree
Example: PLRU for 4-way set associative cache
  Update order: way A  way B  way C  way D
Way A
Way B
Way C
Way D
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
1
1
0
Way B
0
Way A is older than Way B

## Slide 42: Practical Pseudo-LRU:
Each node records which half is older/newer
  - Cache ways are the leaves of the tree
Update nodes on each reference
Key idea: approximated LRU policy with a binary tree
Example: PLRU for 4-way set associative cache
  Update order: way A  way B  way C  way D
Way A
Way B
Way C
Way D
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
1
0
0
Way C
0
Way AB is older than Way CD
Way D is older than Way C
1

## Slide 43: Practical Pseudo-LRU:
Each node records which half is older/newer
  - Cache ways are the leaves of the tree
Update nodes on each reference
Key idea: approximated LRU policy with a binary tree
Example: PLRU for 4-way set associative cache
  Update order: way A  way B  way C  way D
Way A
Way B
Way C
Way D
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
0
0
1
Way D
Way C is older than Way D
0

## Slide 44: Practical Pseudo-LRU:
Each node records which half is older/newer
  - Cache ways are the leaves of the tree
Update nodes on each reference
Follow older pointers to find LRU victim
Key idea: approximated LRU policy with a binary tree
Example: PLRU for 4-way set associative cache
  Update order: way A  way B  way C  way D
Way A
Way B
Way C
Way D
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
0
0
0
Victim block is in Way A
Way A

## Slide 45: Clock algorithm
Simpler implementation
  “Clock” hand points to next page to replace
  If R=0, replace page
  If R=1, set R=0 and advance the clock hand
Continue until page with R=0 is found
  This may involve going all the way around the clock…
Credit: U of pitts
A t=0
B t=4
C t=8
D t=15
E t=21
F t=22
G t=29
H t=30
A t=32
B t=32
C t=32
J t=32
referenced
unreferenced
Notes: https://en.wikipedia.org/wiki/Page_replacement_algorithm#Clock

## Slide 46: Design#4: Write Strategy
Cache
Memory
What happens on a write?

## Slide 47: Handling Cache Hits
Write through vs. Write back
Write through
Write back
Allow cache and memory to be consistent
 Always write the data into both the cache and next level memory
write buffer
 Write-through is always combined with a write buffer; so we can eliminate the overhead
Allow cache and memory to be inconsistent
 Write the data only into the cache block
 Need a dirty bit for each data cache block to tell if it needs to be written back to memory when it is evicted
FIFO
(#entry = 4)

## Slide 48: Handling Cache Write Miss
Write allocate vs. No write allocate
Write allocate
No write allocate
Just write the word into the cache updating both the tag and data, no need to check for cache hit, no need to stall the pipeline
Skip the cache write and just write the word to the next memory level
 Mostly use with write-through cache
Step1: Allocate cacheline and read data from DRAM
When cache miss occurs..
Step2: Write the new data into the allocated cacheline
Directly update the lower level memory

## Slide 49: Types of Caches
There are three types based on associativity
Mapping of data from memory to $ |  |  | 
Complexity of search the cache |  |  | 
Direct mapping (DM)
Set-associative (SA)
Full-associative (FA)
Cache
Cache
Cache
Specific location in the cache (fixed)
Any of a set of locations in the cache
Any location in the cache
Example: 2-way
Fast indexing mechanism | Slightly more involved search mechanism | Extensive hardware resources
DM and FA can be thought as special cases of SA
DM: 1-way SA
FA: All-way SA

## Slide 50: Summary of Caches
 | # of sets | Blocks per set
Direct mapped | # of blocks in cache | 1
Set associative | (# of blocks in cache)/ associativity | Associativity (typically 2 to 16)
Fully associative | 1 | # of blocks in cache
 | Location method | # of comparisons
Direct mapped | Index | 1
Set associative | Index the set; compare set’s tags | Degree of associativity
Fully associative | Compare all blocks tags | # of blocks
Where can a block be placed / found?

## Slide 51: Cache Optimizations
We can improve the cache performance by reducing AMAT!
Average Memory Access Time (AMAT)
  = Hit time + Miss rate x Miss penalty

## Slide 52: Summary of Cache Optimization
Technique | Miss Rate | Miss Pen. | Hit time | Hardware Complexity
Larger Block Size | + | - |  | 0
Higher Associativity | + |  | - | 1
Victim Caches | + |  |  | 2
Pseudo-associative | + |  |  | 2
Hardware Prefetching | + |  |  | 2
Compiler-controlled Pre | + |  |  | 3
Compiler Techniques | + |  |  | 0
Giving Read Misses Priority |  | + |  | 1
Subblock Placement |  | + |  | 1
Early Restart/Crit Wd First |  | + |  | 2
Nonblocking Caches |  | + |  | 3
Second-Level Caches |  | + |  | 2
Small and Simple Caches | - |  | + | 0
Avoiding Address Trans. |  |  | + | 2
Pipelining Writes |  |  | + | 1

## Slide 53: Goal#1: Miss Penalty ↓
Multi-level caches
Critical Word First and early restart
Combining writes
Non-blocking caches
Average Memory Access Time (AMAT)
  = Hit time + Miss rate x Miss penalty

## Slide 54: Technique1: Multi-level Caches
Key idea: fill the gap between the central processing unit and main memory by adding another level in the hierarchy
L1$
Processor
L2$
Main memory
Secondary Memory
Past
Now
Processor
Main memory
Secondary Memory
L3-L4 eDRAM
L1-L2 SRAM
Storage-Class
Memory (SCM)

## Slide 55: Kinds of Cache Hierarchies
Credit: Intel [MICRO’10]
Today’s processors have multi-level cache hierarchies
And multi-level caches can be designed in various ways depending on whether the content of one cache in present in other level of caches
Exclusive
hierarchy
 upper-level blocks must not exist in the lower-level
Non-Inclusive hierarchy
 May contain the upper-level blocks in the lower-level
Inclusive
hierarchy
 upper-level blocks always exist in the lower-level
Upper
Lower
fill
fill
victim
evict
Back-invalidation
Upper
Lower
Upper
Lower
fill
fill
victim
fill
victim
victim
fill

## Slide 56: Technique2: Early Restart & Critical Word First
Key idea: do not wait for the entire block to be loaded before restarting CPU – CPU needs only 1 word
Critical Word First
 Request the missed word first from memory and send it to the CPU as soon as it arrives
Early restart
 As soon as the requested word of the block arrives, send it to the CPU and let the CPU continue execution
0
1
2
3
Block (ex: 32B, 4 words)
0
1
2
3
Resume
L1$
Processor
L2$
4-8 bytes (word)
8-32 bytes (block)
0
1
2
3
0
1
2
3
Resume
Critical word
Critical word

## Slide 57: Technique3: Combining Writes
Intel® 64 and IA-32 Architectures Software Developer’s Manual Volume 3A: System Programming Guide, Part 1、
Background: MTRR (Memory type range register) in x86
  Indicates how accesses to memory ranges by the CPU are cached
    We can simply check with “cat /proc/mtrr”
  There are 5 memory types
Memory Types in x86 | Explanation
UnCacheable (UC) | Bypass all the cache subsystem
UnCacheable Speculative Write-combining (USWC or WC) | Bypasses the caches, excluding write combining buffer (WCB)
WriteBack (WB) | Write the data only into the cache block
Write-Through (WT) | Always write the data into both the cache and next level memory
Write-Protected (WP) | Supervisor-mode access only

## Slide 58: Write Combining Buffer
Processor
Lower level memory
WC buffer
UC mode
Key idea: coalescing writes before or during a long lasting operation like a bus transaction or a cache coherency transaction
Only for USWC (Uncacheable Speculative Write-Combining) memory
  Explicit method (instruction) to use USWC memory type: non-temporal load (movntdqa) and non-temporal store (moventdq)
USWC mode
WB mode
L1$
L2$
LLC
Mem[100]
Mem[108]
Mem[116]
Mem[124]
Mem[400]
Mem[900]
Mem[100]
Mem[400]
Mem[108]
Mem[900]
Mem[116]
Mem[124]
Mem[100]
Mem[108]
Mem[116]
Mem[124]

## Slide 59: Technique4: Non-Blocking Cache
Recall: pipeline stall by cache miss in MIPS
Program
Instruction1
Cycle1
Cycle2
Cycle3
Cycle4
Cycle5
Cycle6
Cycle7
Cycle8
Cycle9
stall
stall
stall
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
Instruction2
IM
Cache miss occurs

## Slide 60: Miss Status Holding Registers(MSHRs)
Key idea: allow for more than one outstanding miss by tracking of cache misses and pending load & stores that refer to that cache block
Miss Handling Architecture (MHA) & Miss Status Holding Register (MSHR)
Banked cache system (L1$, L2$, LLC)
Cache Bank
Cache Bank
Cache Bank
Miss Handling Architecture
MSHR File
MSHR File
MSHR File
Comparators
Address
Hit
Block addr
Valid
LD/ST info
MSHR1
Block addr
Valid
LD/ST info
MSHR2
Block addr
Valid
LD/ST info
MSHRN

## Slide 61: Goal#2: Miss Rate ↓
Hardware prefetching
Compiler techniques
Average Memory Access Time (AMAT)
  = Hit time + Miss rate x Miss penalty

## Slide 62: Technique1: Hardware Prefetching
Real CPUs have multiple prefetches
  Usually closer to the core (easier to detect patterns)
  Prefetching at LLC is hard (cache is banked and hashed)
Source: CSE502 prefetching (stony brook univ.)
Key idea: hardware monitors memory accesses
Processor
Registers
L1 I-Cache
L1 D-Cache
L2 Cache
D-TLB
I-TLB
L3 Cache (LLC)
Intel Core2
Prefetcher
Locations
What’s inside today’s chips
L1D$
  PC-localized stride predictors
  Short-stride predictors within block  prefetch next block
L1I$
  predict future PC
L2$
  Stream buffers
  Adjacent-line prefetch
Notes: Stride prefetching: https://www.cse.iitk.ac.in/users/biswap/CS698Y/lectures/L12.pdf

## Slide 63: Stream Buffer
The pattern of prefetching successive blocks is called sequential prefetching. Stream buffer keeps next-N available in buffer
Processor
L1$
Lower level memory
Stream buffer (FIFO Queue version)
tag
One cache line of data
tag
One cache line of data
tag
One cache line of data
+1
Tail entry
tag
One cache line of data
Notes: https://en.wikipedia.org/wiki/Cache_prefetching#Stream_buffers

## Slide 64: Technique2: Cache-friendly Compiler
Key idea: trying to modify the layout of data structures so that they are accessed in a more cache-friendly manner
Loop Interchange
 Change loops nesting to access data in order stored in memory
Loop Fusion
 Combine 2 independent loops that have same looping and some variables overlap
Merging Array
 Merge 2 arrays into a single array of compound elements
Optimized
/*two sequential arrays*/
int val[SIZE];
int key[SIZE];
struct merge {
int val;
int key;
} merged[SIZE];
for (i=0; i<10K; i++)
a[i] = 1/a[i];
for (i=0; i<10K; i++)
sum = sum + a[i];
 Improves spatial locality
for (i=0; i<10K; i++)
a[i] = 1/a[i];
sum = sum + a[i];
For the second line: hit all
Improves temporal locality
for (j=0; j<N-1; j++)
for (i=0;i<N-1;i++)
x[i][j] = 2*x[i][j]
for (i=0; i<N-1; i++)
for (j=0;j<N-1;j++)
x[i][j] = 2*x[i][j]
Sequential access, not striding
Improves spatial locality

## Slide 65: Goal#3: Hit Time ↓
Avoiding address translation during indexing of the cache (virtual cache)
Way prediction
Trace cache
Average Memory Access Time (AMAT)
  = Hit time + Miss rate x Miss penalty

## Slide 66: Technique1: Virtually Indexed Cache
http://ece-research.unm.edu/jimp/611/slides/chap5_4.html
Key idea: The CPU uses virtual addresses that must be mapped to a physical address. Let’s index cache with virtual address (not physical addr.)
Challenge: process switches require cache purging
  Solution: PID tags
Challenge: Aliasing (two diff virtual addrs may have the same physical addr.)
  Solution: anti-aliasing hardware / page coloring / using the page offset
CPU
Address translation
Virtual cache
Primary memory
CPU
Address translation
Physical cache
Primary memory
VA
PA
VA
PA

## Slide 67: Technique2: Way Prediction
Key idea: make set-associative caches faster by keeping extra bits in cache to predict the “way” or block within the set, of next cache access; branch predictor can override the decision of the way predictor
Example: Way prediction instruction cache (Alpha 21264-like)
PC
0x4
Add
addr
inst
Primary
Instruction
Cache
Sequential Way
Branch Target Way
way
Jump target
Jump control
Notes: http://english.ioa.cas.cn/rh/as/201611/W020161123378291811609.pdf

## Slide 68: Technique3: Trace Cache
Key idea: make an instruction cache faster by packing multiple non-contiguous basic blocks into one contiguous trace cache line
Example: Pentium 4 (NetBurst) Trace Cache
  Trace cache stores decoded and cracked instructions
  Micro-operations (uops): returns 6 uops every other cycle
Instruction Cache
Trace Cache
 | E | F | G
H | I | J | 
 | A | B | 
 |  |  | C
D |  |  | 
Branch
Branch
IC Fetch (5 cycles)
A | B
C
D
E | F | G
H | I | J
A | B | C | D | E | F | G | H | I | J
TC Fetch (1 cycle)
A | B | C | D | E | F | G | H | I | J

## Slide 69: Wrap Up
Different Cache Design and Policies could be chosen based on the target performance

## Slide 70: Cache Parameters in Real μProcessor
 | Intel P4 | AMD Opteron
L1 organization | Split I$ and D$ | Split I$ and D$
L1 cache size | 8KB for D$, 96KB for trace cache (~I$) | 64KB for each of I$ and D$
L1 block size | 64 bytes | 64 bytes
L1 associativity | 4-way set assoc. | 2-way set assoc.
L1 replacement | ~ LRU | LRU
L1 write policy | write-through | write-back
L2 organization | Unified | Unified
L2 cache size | 512KB | 1024KB (1MB)
L2 block size | 128 bytes | 64 bytes
L2 associativity | 8-way set assoc. | 16-way set assoc.
L2 replacement | ~LRU | ~LRU
L2 write policy | write-back | write-back

## Slide 71: More about Cache
Cache partitioning
   How about cache fairness in multi-core/thread environment?
    Cache Allocation Technology (CAT)
    Code and Data Prioritization (CDP)
Cache coherence
   How to make synchronization among multiple local caches (per-core L1$ or L2$); we will learn the protocols in later
    Various protocols: MSI, MESI, MOSI, MOESI, MERSI, MESIF, write-once, Synapse, Berkeley, and Firefly and Dragon protocol
Cache side-channel attack
How about the security issue?
    LLC as covert channel
    Reference: Cache side channel attacks: CPU Design as a security problem [HITBSecConf’16]
Processor 1
L1 cache
Processor 2
L1 cache
L2 cache (shared)
Memory

## Slide 72: Memory Hierarchy Design - Cache Memory -
Jie Zhang
jiez@pku.edu.cn
[Adapted from EE488, Myoungsoo Jung, KAIST]