## Slide 1: Computer Architecture Fall 2024 Lecture 03: RISC-V ALU & Basic Architecture
Jie Zhang
jiez@pku.edu.cn

## Slide 2: RISC-V ALU

## Slide 3: RISC-V Arithmetic Logic Unit (ALU)
Must support the Arithmetic/Logic
operations of the ISA
  add, addi
  sub
  mul, mulh, mulhu, div, divu
  and, andi, nor, or, ori, xor, xori
  beq, bne, slt, slti, sltiu, sltu …
m (operation)
result
A
B
ALU
zero
ovf
With special handling for
  sign extend – addi, andi, slti
  zero extend – lbu, sltiu, ori, xori, sltiu
  no overflow detected – addu, multu, divu, sltiu, sltu

## Slide 4: Review: 2’s Complement Binary Representation
2’sc binary | decimal
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
23 - 1 =
-(23 - 1) =
-23 =
1010
complement all the bits
1011
and add a 1
Note: negate and invert are different!
Negate
Notes: 补码

## Slide 5: A Full Adder
1-bit Full Adder
A
B
S
carry_in
carry_out
S = A  B  carry_in (odd parity function)
carry_out = A&B | A&carry_in | B&carry_in
(majority function)
How can we use it to build a 32-bit adder?
How can we modify it easily to build an adder/subtractor?
A | B | carry_in | carry_out | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Notes: S: 本位和
Carry-in：低位的进位
Carry-out：高位的进位

## Slide 6: A 32-bit Ripple Carry Adder/Subtractor
Remember 2’s complement is just
  complement all the bits
  add a 1 in the least significant bit
A 0111  0111 B - 0110  +
1-bit FA
S0
c0=carry_in
c1
1-bit FA
S1
c2
1-bit FA
S2
c3
c32=carry_out
1-bit FA
S31
c31
. . .
A0
A1
A2
A31
B0
B1
B2
B31
add/sub
B0
control
(0=add,1=sub)
B0 if control = 0, !B0 if control = 1
0001
1001
1
1 0001
and add a 1

## Slide 7: Overflow Detection
Overflow: the result is too large to represent in 32 bits
Overflow occurs when
  adding two positives yields a negative
  or, adding two negatives gives a positive
  or, subtract a negative from a positive gives a negative
  or, subtract a positive from a negative gives a positive
On your own: Prove you can detect overflow by:
  Carry into MSB xor Carry out of MSB, ex for 4-bit signed numbers
1
1
1
1
0
1
0
1
1
0
0
1
1
1
0
0
1
1
+
7
3
0
1
– 6
1
1
0
0
1
0
1
1
+
–4
– 5
7
1
0
Notes: 不是很懂如何检测overflow

## Slide 8: Shift Operations
Also need operations to pack and unpack 8-bit characters into 32-bit words
Shifts move all the bits in a word left or right
sll x5, x6, x7 #x5 = x6 << x7 bits
srl x5, x6, x7 #x5 = x6 >> x7 bits
slli x5, x8, 8 #x5 = x8 << 8 bits
srli x5, x8, 8 #x5 = x8 >> 8 bits
Such shifts are logical because they fill with zeros

## Slide 9: Shift Operations (cont.)
An arithmetic shift (sra) maintain the arithmetic correctness of the shifted value (i.e., a number shifted right one bit should be ½ of its original value; a number shifted left should be 2 times its original value)
  so sra uses the most significant bit (sign bit) as the bit shifted in
  note that there is no need for a sla when using two’s complement number representation
sra x5, x6, x7 #x5 = x6 >> x7 bits
srai x5, x6, 7 #x5 = x6 >> 7 bits
The shift operation is implemented by hardware separate from the ALU
  using a barrel shifter (which would take lots of gates in discrete logic, but is pretty easy to implement in VLSI)
Notes: Sla和sli是一个东西，左移同样是补零
Barrel shifter：桶型移位寄存器

## Slide 10: Multiply
Binary multiplication is just a bunch of right shifts and adds
multiplicand
multiplier
partial
product
array
double precision product
n
2n
n
can be formed in parallel and added in parallel for faster multiplication

## Slide 11: Multiply
First version of the multiplication hardware.
An example of multiplication hardware

## Slide 12: Multiply
An example of multiplication hardware
First version of the multiplication hardware.
Revised version of the multiplication hardware.
The Multiplicand register and ALU have been reduced to 64 bits. Now the product is shifted right. The separate Multiplier register also disappeared. The multiplier is placed instead in the right half of the Product register, which has grown by one bit to 129 bits to hold the carry-out of the adder.

## Slide 13: Multiply
An example of multiplication hardware
The fast multiplication hardware.
Rather than use a single 64-bit adder 63 times, this hardware “unrolls the loop” to use 63 adders and then organizes them to minimize delay.

## Slide 14: RISC-V Multiply Instruction
Multiply produces a double precision product
mul x5, x7,x8 # x5 = x7 * x8 (lower bits)
mulh x6, x7,x8 # x6 = x7 * x8 (higher bits)
Multiplies are done by fast, dedicated hardware and are much more complex (and slower) than adders
Hardware dividers are even more complex and even slower
funct7
rs2
rs1
funct3
rd
opcode

## Slide 15: Division
Division is just a bunch of quotient digit guesses and left shifts and subtracts
dividend
divisor
partial
remainder
array
quotient
n
n
remainder
n
0
0
0
0
0
0

## Slide 16: Division
First version of the division hardware.
An example of division hardware
A revised version is provided in page 391, P&H.

## Slide 17: RISC-V Divide Instruction
Divide generates the reminder and the quotient in separately
div x5, x7, x8 # x5 = x7/x8
rem x6, x7, x8 # x6 = x7%x8
As with multiply, divide ignores overflow so software must determine if the quotient is too large. Software must also check the divisor to avoid division by 0.
funct7
rs2
rs1
funct3
rd
opcode

## Slide 18: Representing Big (and Small) Numbers
What if we want to encode the approx. age of the earth?
  4,600,000,000 or 4.6 x 109
or the weight in kg of one a.m.u. (atomic mass unit)
  0.0000000000000000000000000166 or 1.6 x 10-27
There is no way we can encode either of the above in a 32-bit integer.
Floating point representation (-1)sign x F x 2E
  Still have to fit everything in 32 bits (single precision)
s E (exponent) F (fraction)
1 bit 8 bits 23 bits
  The base (2, not 10) is hardwired in the design of the FPALU
  More bits in the fraction (F) or the exponent (E) is a trade-off between precision (accuracy of the number) and range (size of the number)
x0 - x31
PC
Registers
f0 - f31

## Slide 19: Review: IEEE 754 FP Standard Encoding
Most computers these days conform to the IEEE 754 floating point standard (-1)sign x (1+F) x 2E-bias
  Formats for both single and double precision
  F is stored in normalized form where the msb in the fraction is 1 (so there is no need to store it!) – called the hidden bit
  To simplify sorting FP numbers, E comes before F in the word and E is represented in excess (biased) notation
Single Precision |  | Double Precision |  | Object Represented
E (8) | F (23) | E (11) | F (52) | 
0 | 0 | 0 | 0 | true zero (0)
0 | nonzero | 0 | nonzero | ± denormalized number
± 1-254 | anything | ± 1-2046 | anything | ± floating point number
± 255 | 0 | ± 2047 | 0 | ± infinity
255 | nonzero | 2047 | nonzero | not a number (NaN)
Question:
how to represent 1?
Notes: denormalized number：非规格化数

## Slide 20: Floating Point Addition
Addition (and subtraction)
(F1  2E1) + (F2  2E2) = F3  2E3
  Step 1: Restore the hidden bit in F1 and in F2
  Step 1: Align fractions by right shifting F2 by E1 - E2 positions (assuming E1  E2) keeping track of (three of) the bits shifted out in a round bit, a guard bit, and a sticky bit
  Step 2: Add the resulting F2 to F1 to form F3
  Step 3: Normalize F3 (so it is in the form 1.XXXXX …)
    If F1 and F2 have the same sign  F3 [1,4)  1-bit right shift F3 and increment E3
    If F1 and F2 have different signs  F3 may require many left shifts each time decrementing E3
  Step 4: Round F3 and possibly normalize F3 again
  Step 5: Rehide the most significant bit of F3 before storing the result
Question: how to increase accuracy? Check Page 427-429 in P&H

## Slide 21: RISC-V Floating Point Instructions
RISC-V has a separate Floating Point Register File (f0, f1, …, f31) with special instructions to load to and store from them
flw f1,54(x5) #f1 = Memory[x5+54]
fsw f1,58(x5) #Memory[x5+58] = f1
And supports IEEE 754 single
fadd.s f2,f4,f6
and double precision operations
fadd.d f2,f4,f6
similarly for fsub.s, fsub.d, fmul.s, fmul.d, fdiv.s, fdiv.d
Notes: A single precision register is just the lower half of a double-precision register. Note
that, unlike integer register x0, floating-point register f0 is not hard-wired to the
constant 0.

## Slide 22: RISC-V Floating Point Instructions, Con’t
And floating-point single precision comparison operations
flt.s x5,f2,f4 #if(f2 < f4) x5=1; else x5=0
where lt can also be eq, le
And double precision comparison operations
flt.d x5,f2,f4 #if (f2 < f4) x5=1; else x5=0

## Slide 23: Architecture

## Slide 24: Recall: Processor Organization
Memory
ALU / FPU
Control Unit
Bus Interface Unit
Registers
Fetch
(Store)
Decode
Execute
Datapath
  Components – the functional units and storage (e.g., register file) needed to execute instructions
  Interconnects - components connected so that the instructions can be accomplished and so that data can be loaded from and stored to Memory
Control
  Bring input instructions from Memory
  Issue signals to control the information flow between the Datapath components and to control what operations they perform
  Manage instruction sequencing
needs to have the
needs to
RISC-V instructions we reviewed
Memory-reference
Arithmetic/logical
Control flow

## Slide 25: Register Transfer Level
ALU / FPU
Control Unit
Bus Interface Unit
Registers
RTL is a description of data flow between registers
RTL gives a meaning to the instructions
All instructions are fetched from memory at address PC
Inst. | RTL Description
ADD | 
Load | 
Store | 
Beq | 
PC  PC + 4
Reg(Rd)  Reg(Rs) + Reg(Rt);
Reg(Rt)  MEM[Reg(Rs) + sign_ext(lm16)];
MEM[Reg(Rs)+sign_ext(lm16)] Reg(Rt)
If (Reg(Rs) == Reg(Rt))
PC  PC + 4 + 4 x sign_extend(lm16)
Else
PC PC + 4

## Slide 26: ARM1 Gate-Level Simulation
Source: http://visual6502.org/sim/varm/armgl.html
Let’s check which datapath components exist on RISC-V architecture and how RISC-V instructions work on it.
Instructions are executing

## Slide 27: Datapath Components
Two types of functional hardware elements are needed
Combinational elements: Elements that operate on data
Storage elements: Elements that contain on data
PC
32
32
5
5
5
Registers
Rs
Rt
Rd
BusS
BusT
BusD
64
64
64
Instruction Memory
Address
Instruction
32
32
32
64
Data Memory
Address
Data_in
Data_out
64
Extend
16
64
ALU
64
ALU result
64
64
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
Notes: Combinational elements
  Elements that operate on data
Storage elements
  Sequential or state elements
  Elements that contain data

## Slide 28: Multiplexor
Combinational elements: Elements that operate on data
Storage elements: Elements that contain on data
Extend
16
64
ALU
64
ALU result
64
64
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
PC
32
32
5
5
5
64
64
64
Instruction Memory
Address
Instruction
32
32
32
64
Data Memory
Address
Data_in
Data_out
64
0
1
Mux
A simple multifunction logic unit
Notes: Combinational elements
  Elements that operate on data
Storage elements
  Sequential or state elements
  Elements that contain data

## Slide 29: Adding the Control Signal
Combinational elements: Elements that operate on data
Storage elements: Elements that contain on data
PC
32
32
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
5
5
5
64
64
64
Instruction Memory
Address
Instruction
32
32
32
64
Data Memory
Address
Data_in
Data_out
64
Extend
16
64
ALU
64
ALU result
64
64
0
1
Mux
Selecting the operations / Controlling the flow of data
Write Enable
Mem
Read
Mem
Write
ExtOp
select
ALU control
zero
overflow
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
5
5
5
64
64
64
32
64
Data Memory
Address
Data_in
Data_out
64
Extend
16
64
ALU
64
ALU result
64
64
0
1
Mux
Notes: Combinational elements
  Elements that operate on data
Storage elements
  Sequential or state elements
  Elements that contain data

## Slide 30: Clocking Methodologies for Writes
Synchronize the datapath components in hardware-level
Combinational elements: Elements that operate on data
Storage elements: Elements that contain on data
PC
32
32
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
5
5
5
64
64
64
Instruction Memory
Address
Instruction
32
32
32
64
Data Memory
Address
Data_in
Data_out
64
Extend
16
64
ALU
64
ALU result
64
64
0
1
Mux
Write Enable
Mem
Read
Mem
Write
ExtOp
select
ALU control
zero
overflow
PC
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
Data Memory
Address
Data_in
Data_out
Clk
Clk
Clk

## Slide 31
Aside: More about CPU clock
An internal timing device
Using a quartz crystal, the CPU clock breaths life into the processor by feeding it a constant flow of pulses
Quartz crystal
Analog to digital conversion

## Slide 32
Aside: Meaning of Single Cycle
The clocking methodology defines when signals can be read and when they are written
  An edge-triggered methodology
Typical execution
State
Element 1
Combinational
logic
clock
One clock cycle
State
Element 2
❶ Read contents of state elements
❷ Send values through combinational logic
❸ Write results to one or more state elements
Notes: Clocking methodology: 时钟同步方法 -> 军训的时候迈大步
Combinational logic：组合逻辑
State element：状态单元 -> D触发器，寄存器，存储器

## Slide 33
Aside: Meaning of Single Cycle
With edge-triggered clocking, the target clock cycle must be long enough to accommodate the path from one register through the combinational logic to another register
Combinational logic
Register1
Clk
Register2
Clk
: Clock to the output delay through a register
: The longest delay through combinational logic
: Setup time that inputs to a register must be stable before the arrival of clock edge
: Hold time (that inputs to a register) must hold after the arrival of clock edge
Hold time () is normally satisfied since >
≥ + +

## Slide 34
Instruction Memory
Address
Instruction
32
32
PC
32
32
PC
Clk
32
32
Data Memory
Address
Data_in
Data_out
32
Mem
Read
Mem
Write
Data Memory
Address
Data_in
Data_out
Clk
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
5
5
5
32
32
32
Write Enable
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
Clk
Aside: Write Control Signal
Assumes state elements are written on every clock cycle
  If not, they obviously need explicit a write control signal

## Slide 35: Single Cycle Datapath
Instruction Memory
PC
Fetch
Registers
Decoder
Decode
Data Memory
ALU
Execute

## Slide 36: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory
  updating the PC to hold the address of the next instruction
Read
Address
Instruction
Instruction
Memory
Add
PC
4
  PC is updated every cycle, so it does NOT need an explicit write control signal
  Instruction Memory is read every cycle, so it does NOT need an explicit read control signal

## Slide 37: Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
  reading two values from the Register File
    Register File addresses are contained in the instruction
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit

## Slide 38: Executing R Format Operations
R format operations (add, sub, and, or)
  perform the (op and funct) operation on values in rs1 and rs2
  store the result back into the Register File (into location rd)
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
  The Register File is not written every cycle (e.g. sd), so we need an explicit write control signal for the Register File
funct7
rs2
rs1
funct3
rd
opcode
R format
6
0
11
14
19
24
31
Notes: 回忆一下不同format对应的instruction是啥，它们需要什么样的操作

## Slide 39: Executing Load and Store Operations
Load and store operations involves
  compute memory address by adding the base register (read from the Register File during decode) to the 12-bit ______-extended offset field in the instruction
  store value (read from the Register File during decode) written to the Data Memory
  load value, read from the Data Memory, written to the Register File
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Imm
Gen
MemWrite
MemRead
32
64
signed

## Slide 40: Executing Branch Operations
Branch operations involves
  compare the operands read from the Register File during decode for equality (zero ALU output)
  compute the branch target address by adding the updated PC to the 12-bit signed-extended offset field in the instruction
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Imm
Gen
32
64
Shift
left 1
PC from inst. datapath
Add
Branch
target
address
(to branch control logic)

## Slide 41: Creating a Single Datapath from the Parts
Assemble the datapath segments and add control lines and multiplexors as needed
Single cycle design – fetch, decode and execute each instructions in one clock cycle
  no datapath resource can be used more than once per instruction, so some must be duplicated (e.g., separate Instruction Memory and Data Memory, several adders)
  multiplexors needed at the input of shared elements with control lines to do the selection
  write signals to control writing to the Register File and Data Memory
Cycle time is determined by length of the longest path
Notes: 我们如何能把刚刚提到的模块加在一起 -> 可以增加控制单元和复用模块
Multiplexors -> 多路选择器
Single-cycle -> 单周期

## Slide 42: R-type and Memory Access
MemtoReg
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Imm
Gen
32
64
ALUSrc
MUX
MUX
Notes: 可以先回忆一下R-type的指令

## Slide 43: Adding the Control
Selecting the operations to perform (ALU, Register File and Memory read/write)
Controlling the flow of data (multiplexor inputs)
Observations
  op field always in bits 6-0
  addr of registers to be read are always specified by the rs1 field (bits 19-15) and rs2 field (bits 24-20);
  addr. of register to be written is in rd (bits 11-7)
  Another operand can also be a 12-bit offset for branch or load-store instructions.
funct7
rs2
rs1
funct3
rd
opcode
immediate
R format
I format
S format
rs1
funct3
rd
opcode
imm[11:5]
rs2
rs1
funct3
imm[4:0]
opcode
imm[12,10:5]
rs2
rs1
funct3
imm[4:1,11]
opcode
SB format
6
0
11
14
19
24
31

## Slide 44: Single Cycle Datapath with Control Unit
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Imm
Gen
32
64
MemtoReg
ALUSrc
Shift
left 1
Add
PCSrc
ALU
control
1
1
0
0
0
1
ALUOp
Instr[30,14-12]
Instr[31-0]
Instr[19-15]
Instr[24-20]
Control
Unit
Instr[6-0]
Branch
Instr[11-7]

## Slide 45: R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Imm
Gen
32
64
MemtoReg
ALUSrc
Shift
left 1
Add
PCSrc
ALU
control
1
1
0
0
0
1
ALUOp
Instr[30,14-12]
Instr[31-0]
Instr[19-15]
Instr[24-20]
Control
Unit
Instr[6-0]
Branch
Instr[11-7]

## Slide 46: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Imm
Gen
32
64
MemtoReg
ALUSrc
Shift
left 1
Add
PCSrc
ALU
control
1
1
0
0
0
1
ALUOp
Instr[30,14-12]
Instr[31-0]
Instr[19-15]
Instr[24-20]
Control
Unit
Instr[6-0]
Branch
Instr[11-7]

## Slide 47: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Imm
Gen
32
64
MemtoReg
ALUSrc
Shift
left 1
Add
PCSrc
ALU
control
1
1
0
0
0
1
ALUOp
Instr[30,14-12]
Instr[31-0]
Instr[19-15]
Instr[24-20]
Control
Unit
Instr[6-0]
Branch
Instr[11-7]

## Slide 48: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Imm
Gen
32
64
MemtoReg
ALUSrc
Shift
left 1
Add
PCSrc
ALU
control
1
1
0
0
0
1
ALUOp
Instr[30,14-12]
Instr[31-0]
Instr[19-15]
Instr[24-20]
Control
Unit
Instr[6-0]
Branch
Instr[11-7]

## Slide 49: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Imm
Gen
32
64
MemtoReg
ALUSrc
Shift
left 1
Add
PCSrc
ALU
control
1
1
0
0
0
1
ALUOp
Instr[30,14-12]
Instr[31-0]
Instr[19-15]
Instr[24-20]
Control
Unit
Instr[6-0]
Branch
Instr[11-7]

## Slide 50: Control Signal

## Slide 51: Single Cycle Disadvantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
Cycle 1
Cycle 2
Load
Store
Waste
  In particular, its’ problematic for more complex instructions like floating point multiply

## Slide 52: Single Cycle Disadvantages
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
RegWrite
Register File
Write Data
Read Addr 1
Read Addr 2
Write Addr
Read
Data 1
Read
Data 2
MemtoReg
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc
ovf
zero
ALUCtrl
ALU
Read
Address
Instruction
Instruction
Memory
PC
4
ADD
ADD
ALU
Notes: Advantages: Is simple and easy to understand

## Slide 53: Multi-Cycle Datapath

## Slide 54: Recall: Single Cycle Processor
RegWrite
Register File
Write Data
Read Addr 1
Read Addr 2
Write Addr
Read
Data 1
Read
Data 2
Sign
Extend
16
MemtoReg
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
32
ALUSrc
ovf
zero
ALUCtrl
ALU
Read
Address
Instruction
Instruction
Memory
PC
4
ADD
Fetch
Decode
Execute

## Slide 55: Challenges of Single Cycle
We can get a CPI of 1 (for most instructions)
But clock cycle time is long
  It must be long enough to complete the most time-consuming instruction
Load
Store
Waste
One cycle is determined to accommodate a long critical path (laggard)
Clock

## Slide 56: Solution: Multicycle Datapath Approach
Cycle1
Cycle2
Cycle3
Cycle4
Cycle5
Cycle6
Cycle7
Cycle8
Cycle9
Cycle10
Single cycle implementation
Multi-cycle implementation
Clock
Load
Store
ADD
Clock
Load
Store
Cycle 1
Cycle 2
Waste
This multicycle clock machine slower than 1/5th of the single cycle one due to implementation issues (will discussed)
But, it eventually removes the wasted time

## Slide 57: Design Principles of Multicycle Datapath
Q1. How to let an instruction take more than 1 clock cycle to complete?
A. Break up an instruction into small steps
Q2. How to efficiently manage the datapath components? (Removes unnecessary resource duplication)
A. Allow functional units can be used more than once per instruction (but in a different cycle)
Q3. For the single cycle, control signals could be determined from opcode.. How about multicycle?
A. Use a finite state machine (FSM) for control

## Slide 58: Break up An Instruction into Multi-Steps
Ifetch: Instruction Fetch and Update PC
Dec: Instruction Decode, Register Read, Sign Extend Offset
Exec: Execute R-type; Calculate Memory Address; Branch Comparison; Branch and Jump Completion
Mem: Memory Read; Memory Write Completion; R-type Completion (RegFile write)
WB: Memory Read Completion (RegFile write)
Cycle1
Cycle2
Cycle3
Cycle4
Cycle5
Clock
Load
Cycle6
Cycle7
Cycle8
Cycle9
Cycle10
Store
ADD
Dec
IFetch
Mem
Exec
WB
Balance the amount of work to be done in each step
Restrict each cycle to enable only one major functional unit
Load (5 cycles)
Dec
IFetch
Exec
Store (4 cycles)
Mem

## Slide 59: Design/Support for Multi-Step Instructions
[REMIND] Clock methodologies
State
Element 1
Combinational
logic
clock
One clock cycle
State
Element 2
❶ Read contents of state elements
❷ Send values through combinational logic
❸ Write results to one or more state elements
   At the end of a cycle, let’s store value(s), which will be needed in a next cycle into an internal register.

## Slide 60: Design/Support for Multi-Step Instructions
Functional units can be used on different clock cycles
  Only need one memory – but only one memory access/cycle
  Need only one ALU/adder – but only one ALU operation/cycle
Additional internal state registers
  IR (Instruction register), MDR (Memory Data Register)
  A, B (regfile read data registers), ALUout (ALU output register)
PC
Memory
Address
Data_in
Data_out
IR
MDR
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
A
B
ALU
ALUout

## Slide 61: Design/Support for Multi-Step Instructions
Functional units can be used on different clock cycles
  Only need one memory – but only one memory access/cycle
  Need only one ALU/adder – but only one ALU operation/cycle
Additional internal state registers
  IR (Instruction register), MDR (Memory Data Register)
  A, B (regfile read data registers), ALUout (ALU output register)
Memory
Address
Data_in
Data_out
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
ALU
PC
IR
MDR
A
B
ALUout
Clock
Read PC
Write memory data to register
Memory
Address
Data_in
Data_out
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
Write memory data to register
Read
Write memory data to register
Read
ALU

## Slide 62: Finite State Machine for Control
Opcode bits tell you on what operation the ALU should be doing, but not what instruction cycle is to be done in next
Finite state machine (FSM) for control
  A set of states (the current state stored in State Register)
  Next state function (determined by the current state and input)
  Output function (determined by the current state and input)
Control logic (FSM)
State Reg
Inst
Opcode
Next State
. . .
. . .
Datapath
control
points
. . .

## Slide 63: Finite State Machine for Control
Control logic (FSM)
Opcode bits tell you on what operation the ALU should be doing, but not what instruction cycle is to be done next
Finite state machine (FSM) for control
  A set of states (the current state stored in State Register)
  Next state function (determined by current state and the input)
  Output function (determined by current state and the input)
State Reg
Inst
Opcode
Next State
. . .
. . .
Datapath
control
points
. . .
Control logic (FSM)
Example

## Slide 64: The Multicycle Datapath with Control Signals
Memory
Address
Data_in
Data_out
Registers
Read
Addr1
Read
Addr2
Write Addr
Read
Data1
Read
Data2
Write Data
0
1
IR
MDR
A
B
ALU
ALUout
0
1
2
3
ALU Ctrl
Shift left 2
0
1
PC
2
0
1
Inst[15-0]
Inst[5-0]
Sign
Extend
32
Shift
Left 2
4
Inst[25-0]
28
PC[31-28]
Inst[31-26]
zero
PCWriteCond
PCWrite
PC Update
IorD
MemRead
MemWrite
IRWrite
RegDst
RegWrite
ALUSrcA
ALUSrcB
ALUOp
PCSource
MemtoReg
Mem control
Reg control
Mux control
Control unit
ALU
control

## Slide 65: Multicycle Advantages & Disadvantages
+) Uses the clock cycle efficiently – each clock cycle considers the instruction “step” (not the longest instruction like what single cycle needs to do)
+) Multicycle allows to use functional units more than once per instruction (across different cycles)
-) But, it requires additional internal state registers, more muxes, and complicated (FSM) control
Cycle1
Cycle2
Cycle3
Cycle4
Cycle5
Cycle6
Cycle7
Cycle8
Cycle9
Cycle10
Clock
Load
Store
ADD
Dec
IFetch
Mem
Exec
WB
Dec
IFetch
Exec
Load (5 cycles)
Store (4 cycles)
Mem

## Slide 66: Pipelining
Still multicycle is slow..
Need for SPEED!
(Throughput viewpoint, not latency)
Multicycle
Pipelining

## Slide 67: Oil Transport Analogy for Strategy
Plan A: Move 1,000,000 gallons of oil at a time
  Buy a tanker ship, then repeat:
    Fill with oil, sail for 30 days, empty, go back
Plan B: Move 100 gallons of oil at a time
  Buy a speedboat, then repeat:
    Take barrel of oil, sail for 2 days, unload, go back
Plan C:
Single-cycle
Multi-cycle
Pipeline

## Slide 68: Student Cafeteria, KAIMARU Analogy
Multi cycle processor
Rice
Kimchi
Soup
Egg
Pipeline processor

## Slide 69: Design Principles of Pipeline Datapath
Q1. In contrast to multicycle, 5 stages (IF, ID,EX,MEM,WB) require enabling some Datapath components at the same time
A. Like single cycle Datapath, duplicates several Datapath components again
Q2. How to execute multiple instructions at the same time? (Program counter is updated on every cycle)
A. Use additional intermediate registers to record the PC and Instruction
Q3. Similar to Q2, the functionality of control signals, which are required for each instruction, varies.. How can we handle the signals?
A. Let’s propagate the control signals through the pipeline by passing them via the pipeline registers, along with the other data
We want to overlap multiple instructions. What should be modified from multicycle Datapath?

## Slide 70: Design1: Duplicate Datapath Components
Equivalent to the original single-cycle Datapath
  Separate memories for instructions and data
  Two adders for PC-based computations + one ALU
Instruction
memory
Read
address
Inst.
[31-0]
Data
memory
Address
Write
data
Read
data
ADD
ALU
Zero
Result

## Slide 71: Design1: Duplicate Datapath Components
But, one register file is enough to support both the ID and WB
  Reads and writes go to separate ports on the register file
  Writes occur in the first half of the cycle, reads occur in the second half
Instruction
memory
Read
address
Inst.
[31-0]
Data
memory
Address
Write
data
Read
data
ADD
ALU
Zero
Result
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
WRITE memory data to register
READ memory data to register

## Slide 72: Design2: Pipeline Registers
Any data values required in later stages must be propagated through the pipeline registers
Simplify diagrams consider the registers as just one big pipeline register between each stage (IF/ID, ID/EX, EX/MEM, MEM/WB)
Instruction
memory
Read
address
Inst.
[31-0]
Data
memory
Address
Write
data
Read
data
ADD
ALU
Zero
Result
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
IF/ID
ID/EX
EX/MEM
MEM/WB
PCWB
PCMEM
PCRF
PC
PCALU
IRWB
IRMEM
IRRF
IRALU
OutMEM
A
B
OutWB
DALU
DMEM
IR: Instruction Register
A: RegData1
B: RegData2
Out: ALU output
D: RegData2
(will be memory address)

## Slide 73: Aside: Example of Value Forwarding
Destination register
  The rd field of the instruction, retrieved in the IF, determines the destination register. However, such the register value isn’t propagated from the IF stage to the WB stage.
  Thus, the rd field must be passed through all of the pipeline stages
Instruction
memory
Read
address
Inst.
[31-0]
Data
memory
Address
Write
data
Read
data
ADD
ALU
Zero
Result
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
IF/ID
ID/EX
EX/MEM
MEM/WB
Instr [15 - 11]
Instr [20 - 16]
0
1
RegDst
Rd
Rd
Rd
Rd

## Slide 74: Design3: Control Signal Propagation
The control signals are generated in the same way as in the single-cycle processor. But, note that some of the control signals won’t be needed for some next-level stages and clock cycles.
IF/ID
ID/EX
EX/MEM
MEM/WB
Instruction
memory
Read
address
Inst.
[31-0]
Instr [15 - 0]
RegWrite
Instr [15 - 11]
Instr [20 - 16]
PCSrc
PC
4
ADD
1
0
Sign
Extend
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
0
1
RegDst
0
1
MemtoReg
0
1
ALUSrc
Shift
left2
ADD
ALU
Zero
Result
ALUOp
MemRead
MemWrite
Data
memory
Address
Write
data
Read
data
WB
WB
WB
MEM
MEM
EX
Control
EX: ALUSrc
ALUOp
RegDst
MEM: ALUSrc
ALUOp
RegDst
WB: MemRead
MemWrite
PCSrc

## Slide 75: An Example Execution Sequence
Sample sequence of instructions to execute
1000: lw $8, 4($29)
1004: sub $2, $4, $5
1008: and $9, $10, $11
1012: or $16, $17, $18
1016: add $13, $14, $0
Pipeline terminology
  The pipeline depth: number of stages – in this case, five
  In the first 4 cycles, the pipeline is filling, since there are unused functional units
  In cycle 5, the pipeline is full. All HW units are in use.
  In cycle 6-9, the pipeline is emptying; if there are more instructions, such pipeline can bring out an output at every single cycle

## Slide 76: Cycle 1 (Filling the Pipeline)
IF/ID
Instruction
memory
Read
address
Inst.
[31-0]
PCSrc
PC
4
ADD
1
0
IF
ID/EX
EX/MEM
MEM/WB
Instr [15 - 0]
RegWrite
Instr [15 - 11]
Instr [20 - 16]
Sign
Extend
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
0
1
RegDst
0
1
MemtoReg
0
1
ALUSrc
Shift
left2
ADD
ALU
Zero
Result
ALUOp
MemRead
MemWrite
Data
memory
Address
Write
data
Read
data
WB
WB
WB
MEM
MEM
EX
Control
ID
EX
MEM
WB
Instr1

## Slide 77: Cycle 2 (Filling the Pipeline)
IF/ID
Instruction
memory
Read
address
Inst.
[31-0]
PCSrc
PC
4
ADD
1
0
IF
ID/EX
Instr [15 - 0]
RegWrite
Instr [15 - 11]
Instr [20 - 16]
Sign
Extend
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
WB
MEM
EX/MEM
MEM/WB
0
1
RegDst
0
1
MemtoReg
0
1
ALUSrc
Shift
left2
ADD
ALU
Zero
Result
ALUOp
MemRead
MemWrite
Data
memory
Address
Write
data
Read
data
EX
MEM
WB
WB
WB
MEM
EX
Control
ID
Instr2
Instr1

## Slide 78: Cycle 3 (Filling the Pipeline)
IF/ID
Instruction
memory
Read
address
Inst.
[31-0]
PCSrc
PC
4
ADD
1
0
IF
ID/EX
Instr [15 - 0]
RegWrite
Instr [15 - 11]
Instr [20 - 16]
Sign
Extend
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
WB
MEM
EX/MEM
0
1
RegDst
0
1
ALUSrc
Shift
left2
ADD
ALU
Zero
Result
ALUOp
EX
MEM/WB
0
1
MemtoReg
MemRead
MemWrite
Data
memory
Address
Write
data
Read
data
MEM
WB
WB
WB
MEM
EX
Control
ID
Instr3
Instr2
Instr1

## Slide 79: Cycle 4 (Filling the Pipeline)
IF/ID
Instruction
memory
Read
address
Inst.
[31-0]
PCSrc
PC
4
ADD
1
0
IF
ID/EX
Instr [15 - 0]
RegWrite
Instr [15 - 11]
Instr [20 - 16]
Sign
Extend
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
WB
MEM
EX/MEM
0
1
RegDst
0
1
ALUSrc
Shift
left2
ADD
ALU
Zero
Result
ALUOp
EX
MemRead
MemWrite
Data
memory
Address
Write
data
Read
data
MEM
WB
MEM/WB
0
1
MemtoReg
WB
WB
MEM
EX
Control
ID
Instr4
Instr3
Instr2
Instr1

## Slide 80: Cycle 5 (Full)
IF/ID
Instruction
memory
Read
address
Inst.
[31-0]
PCSrc
PC
4
ADD
1
0
IF
ID/EX
EX/MEM
MEM/WB
Instr [15 - 0]
RegWrite
Instr [15 - 11]
Instr [20 - 16]
Sign
Extend
Read
Data1
Read
Data2
Read
Addr1
Read
Addr2
Write Addr
Write Data
Registers
0
1
RegDst
0
1
MemtoReg
0
1
ALUSrc
Shift
left2
ADD
ALU
Zero
Result
ALUOp
MemRead
MemWrite
Data
memory
Address
Write
data
Read
data
WB
WB
WB
MEM
MEM
EX
Control
ID
EX
MEM
WB
Instr5
Instr4
Instr3
Instr2
Instr1

## Slide 81: The Pipelining Paradox
Pipelining does not improve the any single instruction latency
  Each instruction actually takes longer to execute than in a single-cycle Datapath!
[REMIND] Meaning of Single Cycle in Lecture 3
  Ts: Setup time that inputs to a register
  Th: Hold time that inputs to a register
  Latch at the end of each stage adds latency!

## Slide 82
Instruction takes 5 cycles now!
Instruction latency longer now
  Latch at end of each stage adds latency
  Longest stage determines clock cycle time
  Example:
  But we are after instruction throughput, not latency!!!
IF | 1.0 ns
ID | 0.6 ns
EX | 0.9 ns
MEM | 1.2 ns
WB | 0.4 ns
Design | Cycle time | # of cycles | Inst Latency
1-stage | 4.1 ns (sum) | 1 | 4.1 ns
5-stage | 1.2 ns (max) | 5 | 6.0 ns
Is it Faster?

## Slide 83: Performance with Pipelining
We finish one instruction per cycle
  After the initial warm-up period
Instruction throughput
  Latch at end of each stage adds latency
  Longest stage determines clock cycle time
  Example:
                Speedup due to pipelining: 3.42
                Note: ideally it would be 5
Design | Cycle time | Inst/Cycle
1-cycle | 4.1 ns (sum) | 1
Pipeline | 1.2 ns (max) | 1
Performance with Pipelining
IF | 1.0 ns
ID | 0.6 ns
EX | 0.9 ns
MEM | 1.2 ns
WB | 0.4 ns

## Slide 84: Ideal Speedup
Instead, pipelining increase the throughput; again, every cycle, it can deliver the output
As we can execute up to five instructions simultaneously, the ideal speedup equals the pipeline depth
Q) Why the pipelining speedup “less than” 5?
A) The pipeline stages are imbalanced
ALU
IM
Reg
Reg
DM

## Slide 85: Intel x86 Pipeline History
Source: Pipeline Architecture since 1985
Let’s increase processor throughput by increasing pipeline depth
i486
Pentium
Willamette
P4
Prescott
Core 2 Conroe
Core 2 Yorkfield
Core i7 Gulftown
Pipeline depths and frequency at introduction
  What happen here?

## Slide 86: Limits to Pipelining1 – Power Issue
Too many thing happening at once
  Melt your chip!
Must disable parts of the system that are not being used
  Clock Gating, Asynchronous Design, Low Voltage Swings,…
Vdd
Clk
Propagation Delay
Clk-Q
Setup
Time Slack
Clk
Notes:   Traditionally pipelining was used to increase clock frequency for performance.
  But the time slack obtained from pipelining can also be used to reduce power consumption.
  Supply voltage scaling is one of the most effective delay-power tradeoff techniques.
  Our target digital system has highly parallel computation and we assume that it is pipelinable without CPI loss.
  And the system has fixed throughput requirement and clock frequency is fixed.
  In this work, we show how power-optimal pipelining varies for different operating regimes in deep submicron technology.
  We explore the effects of Vdd, Vth, activity factor, and clock gating.

## Slide 87: Limits to Pipelining2 – Hazard Issue
Hazards prevent next instruction from executing during its designated clock cycle
3 types of hazard: Structural hazards, Data hazards, Control hazards

## Slide 88: Hazards

## Slide 89: Graphically Representing a Pipeline
Can help with answering questions like:
  How many cycles does it take to execute this code?
  What is the ALU doing during cycle 4?
  Is there a hazard, why does it occur, and how can it be fixed?
ALU
IM
Reg
DM
Reg

## Slide 90: Why Pipeline? For Performance!
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Once the pipeline is full, one instruction is completed every cycle, so CPI = 1
Time to fill the pipeline

## Slide 91: Can Pipelining Get Us Into Trouble?
Yes: Pipeline Hazards
  structural hazards: attempt to use the same resource by two different instructions at the same time
  data hazards: attempt to use data before it is ready
    An instruction’s source operand(s) are produced by a prior instruction still in the pipeline
  control hazards: attempt to make a decision about program control flow before the condition has been evaluated and the new PC target address calculated
    branch instructions
Can always resolve hazards by waiting
  pipeline control must detect the hazard
  and take action to resolve hazards

## Slide 92: A Single Memory Would Be a Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
ld
Inst 1
Inst 2
Inst 4
Inst 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Reading data from memory
Reading instruction from memory
Fix with separate instr and data memories (I$ and D$)

## Slide 93: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
add x1,
Inst 1
Inst 2
add x2,x1,
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg

## Slide 94: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 1
Inst 2
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix register file access hazard by doing reads in the second half of the cycle and writes in the first half
add x1,
add x2,x1,

## Slide 95: Register Usage Can Cause Data Hazards
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
add x1,
sub x4,x1,x5
and x6,x1,x7
xor x4,$1,x5
or x8,x1,x9
Read after write data hazard
I
n
s
t
r.
O
r
d
e
r

## Slide 96: Loads Can Cause Data Hazards
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
ld x1,4(x2)
sub x4,x1,x5
and x6,x1,x7
xor x4,x1,x5
or x8,x1,x9
Read after write data hazard
I
n
s
t
r.
O
r
d
e
r
Notes: Read after read?
Write after write?
Write after read?

## Slide 97: One Way to “Fix” a Data Hazard
stall
stall
I
n
s
t
r.
O
r
d
e
r
add x1,
ALU
IM
Reg
DM
Reg
sub x4,x1,x5
and x6,x1,x7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Can fix data hazard by waiting – stall – but impacts CPI

## Slide 98: Another Way to “Fix” a Data Hazard
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix data hazards by forwarding results as soon as they are available to where they are needed
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
I
n
s
t
r.
O
r
d
e
r
add x1,
sub x4,x1,x5
and x6,x1,x7
xor x4,x1,x5
or x8,x1,x9

## Slide 99: Forwarding with Load-use Data Hazards
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Will still need one stall cycle even with forwarding
I
n
s
t
r.
O
r
d
e
r
ld x1,4(x2)
sub x4,x1,x5
and x6,x1,x7
xor x4,x1,x5
or x8,x1,x9
Notes: Forward：前递

## Slide 100: Data Forwarding (aka Bypassing)
Take the result from the earliest point that it exists in any of the pipeline state registers and forward it to the functional units (e.g., the ALU) that need it that cycle
For ALU functional unit: the inputs can come from any pipeline register rather than just from ID/EX by
  adding multiplexors to the inputs of the ALU
  connecting the Rd write data in EX/MEM or MEM/WB to either (or both) of the EX’s stage Rs and Rt ALU mux inputs
  adding the proper control hardware to control the new MUXes
Other functional units may need similar forwarding logic (e.g., the DM)
With forwarding can achieve a CPI of 1 even in the presence of data dependencies

## Slide 101: Data Forwarding Control Conditions
EX/MEM hazard:
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs1))
ForwardA = 10
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs2))
ForwardB = 10
Forwards the result from the previous instr. to either input of the ALU
Forwards the result from the second previous instr. to either input of the ALU
MEM/WB hazard:
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs1))
ForwardA = 01
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs2))
ForwardB = 01
Note:
ID/EX = 00， EX/MEM = 10，MEM/WB = 01
Notes: 前递的多路选择器：ID/EX = 00， EX/MEM = 10，MEM/WB = 01

## Slide 102: Forwarding Illustration
I
n
s
t
r.
O
r
d
e
r
add x1,
sub x4,x1,x5
and x6,x7,x1
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
EX/MEM hazard forwarding
MEM/WB hazard forwarding

## Slide 103: Yet Another Complication!
I
n
s
t
r.
O
r
d
e
r
add x1,x1,x2
ALU
IM
Reg
DM
Reg
add x1,x1,x3
add x1,x1,x4
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Another potential data hazard can occur when there is a conflict between the result of the WB stage instruction and the MEM stage instruction – which should be forwarded?

## Slide 104: Corrected Data Forwarding Control Conditions
MEM/WB hazard:
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRs)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
ForwardA = 01
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRs1)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs1))
ForwardB = 01

## Slide 105: Memory-to-Memory Copies
For loads immediately followed by stores (memory-to-memory copies) can avoid a stall by adding forwarding hardware from the MEM/WB register to the data memory input.
  Would need to add a Forward Unit and a mux to the memory access stage
I
n
s
t
r.
O
r
d
e
r
ld x1,4(x2)
ALU
IM
Reg
DM
Reg
sd x1,4(x3)
ALU
IM
Reg
DM
Reg

## Slide 106: Forwarding with Load-use Data Hazards
stall
I
n
s
t
r.
O
r
d
e
r
ld x1,4(x2)
sub x4,x1,x5
and x6,x1,x7
xor x4,x1,x5
or x8,x1,x9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
sub x4,x1,x5
and x6,x1,x7
xor x4,x1,x5
or x8,x1,x9

## Slide 107: Load-use Hazard Detection Unit
Need a Hazard detection Unit in the ID stage that inserts a stall between the load and its use
ID Hazard Detection
if (ID/EX.MemRead
and ((ID/EX.RegisterRd = IF/ID.RegisterRs1)
or (ID/EX.RegisterRd = IF/ID.RegisterRs2)))
stall the pipeline
The first line tests to see if the instruction now in the EX stage is a ld; the next two lines check to see if the destination register of the ld matches either source register of the instruction in the ID stage (the load-use instruction)
After this one cycle stall, the forwarding logic can handle the remaining data hazards

## Slide 108: Stall Hardware
Along with the Hazard Unit, we have to implement the stall
Prevent the instructions in the IF and ID stages from progressing down the pipeline – done by preventing the PC register and the IF/ID pipeline register from changing
  Hazard detection Unit controls the writing of the PC (PC.write) and IF/ID (IF/ID.write) registers
Insert a “bubble” between the lw instruction (in the EX stage) and the load-use instruction (in the ID stage) (i.e., insert a noop in the execution stream)
  Set the control bits in the EX, MEM, and WB control fields of the ID/EX pipeline register to 0 (noop). The Hazard Unit controls the mux that chooses between the real control values and the 0’s.
Let the lw instruction and the instructions after it in the pipeline (before it in the code) proceed normally down the pipeline

## Slide 109: Datapath Modifications with Forwarding and Hazard Detection

## Slide 110: Control Hazards
When the flow of instruction addresses is not sequential (i.e., PC = PC + 4); incurred by change of flow instructions
  Conditional branches (beq)
Possible approaches
  Stall (impacts CPI)
  Move decision point as early in the pipeline as possible, thereby reducing the number of stall cycles
  Delay decision (requires compiler support)
  Predict and hope for the best !
Control hazards occur less frequently than data hazards, but there is nothing as effective against control hazards as forwarding is for data hazards

## Slide 111: Branch Instructions Cause Control Hazards
I
n
s
t
r.
O
r
d
e
r
ld
Inst 4
Inst 3
beq
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards

## Slide 112: One Way to “Fix” a Control Hazard
stall
stall
stall
I
n
s
t
r.
O
r
d
e
r
beq
ALU
IM
Reg
DM
Reg
ld
ALU
IM
Reg
DM
Reg
ALU
Inst 3
IM
Reg
DM
Fix branch hazard by waiting – stall – but affects CPI

## Slide 113: Moving Branch Decisions Earlier in Pipe
Design: Add hardware to compute the branch target address and evaluate the branch decision to the ____ stage
  Reduces the number of stall (flush) cycles to ____ ?
    But now need to add forwarding hardware in ID stage
  Computing branch target address can be done in parallel with RegFile read
  Comparing the registers can’t be done until after RegFile read, so comparing and updating the PC adds a mux, a comparator, and an and gate to the ID timing path
For deeper pipelines, branch decision points can be even later in the pipeline, incurring more stalls
ID
1

## Slide 114: ID Branch Forwarding Issues
MEM/WB “forwarding” is taken care of by the normal RegFile write before read operation
WB add x1,
MEM add x3,
EX add x4,
ID beq x1,x2,Loop
IF next_seq_instr
Need to forward from the EX/MEM pipeline stage to the ID comparison hardware for cases like
WB add $3,
MEM add x1,
EX add $4,
ID beq x1,x2,Loop
IF next_seq_instr
if (IDcontrol.Branch
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = IF/ID.RegisterRs1))
ForwardC = 1
if (IDcontrol.Branch
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = IF/ID.RegisterRs2))
ForwardD = 1
Forwards the result from the second previous instr. to either input of the compare

## Slide 115: ID Branch Forwarding Issues, con’t
If the instruction immediately before the branch produces one of the branch source operands, then a stall needs to be inserted (between the beq and add) since the EX stage ALU operation is occurring at the same time as the ID stage branch compare operation
  “Bounce” the beq (in ID) and next_seq_instr (in IF) in place (ID Hazard Unit deasserts PC.Write and IF/ID.Write)
  Insert a stall between the add in the EX stage and the beq in the ID stage by zeroing the control bits going into the ID/EX pipeline register (done by the ID Hazard Unit)
WB add x3,
MEM add x4,
EX add x1,
ID beq x1,$2,Loop
IF next_seq_instr

## Slide 116: Static Branch Prediction
Resolve branch hazards by assuming a given outcome and proceeding without waiting to see the actual branch outcome
Predict not taken – always predict branches will not be taken, continue to fetch from the sequential instruction stream, only when branch is taken does the pipeline stall
  If taken, flush instructions after the branch (earlier in the pipeline)
    in IF, ID, and EX stages if branch logic in MEM – three stalls
    in IF and ID stages if branch logic in EX – two stalls
    in IF stage if branch logic in ID – one stall
  Ensure that those flushed instructions haven’t changed the machine state – automatic in the pipeline since machine state changing operations are at the tail end of the pipeline (MemWrite (in MEM) or RegWrite (in WB))
  Restart the pipeline at the branch destination
  30-40% accuracy…not so good

## Slide 117: ASIDE: Two “Types” of Stalls
Noop instruction (or bubble) inserted between two instructions in the pipeline (as done for load-use situations)
  Keep the instructions earlier in the pipeline (later in the code) from progressing down the pipeline for a cycle (“bounce” them in place with write control signals)
  Insert noop by zeroing control bits in the pipeline register at the appropriate stage
  Let the instructions later in the pipeline (earlier in the code) progress normally down the pipeline
Flushes (or instruction squashing) were an instruction in the pipeline is replaced with a noop instruction

## Slide 118: Static Branch Prediction, con’t
Resolve branch hazards by assuming a given outcome and proceeding
Predict taken – predict branches will always be taken
  60-70% accuracy
  Predict taken always incurs one stall cycle (if branch destination hardware has been moved to the ID stage)
  Is there a way to “cache” the address of the branch target instruction ??
As the branch penalty increases (for deeper pipelines), a simple static prediction scheme will hurt performance. With more hardware, it is possible to try to predict branch behavior dynamically during program execution
Dynamic branch prediction – predict branches at run-time using run-time information

## Slide 119: Dynamic Branch Prediction
Need to know two things
– Whether the branch is taken or not (direction)
– The target address if it is taken (target)
Direct jumps, Function calls
– Direction known (always taken), target easy to compute
Conditional Branches (typically PC-relative)
– Direction difficult to predict, target easy to compute
Indirect jumps, function returns
– Direction known (always taken), target difficult

## Slide 120: Dynamic Branch Prediction
A branch prediction buffer (aka branch history table (BHT)) in the IF stage addressed by the lower bits of the PC, contains a bit passed to the ID stage through the IF/ID pipeline register that tells whether the branch was taken the last time it was executed
  Prediction bit may predict incorrectly (may be a wrong prediction for this branch this iteration or may be from a different branch with the same low order PC bits) but it doesn’t affect correctness, just performance
    Branch decision occurs in the ID stage after determining that the fetched instruction is a branch and checking the prediction bit
  If the prediction is wrong, flush the incorrect instruction(s) in pipeline, restart the pipeline with the right instruction, and invert the prediction bit
    A 4096-bit BHT varies from 1% misprediction (nasa7, tomcatv) to 18% (eqntott)

## Slide 121: 1-bit Predictors

## Slide 122: 1-bit Predictors

## Slide 123: 2-bit Predictors
Predict
Taken
Predict
Not Taken
Predict
Taken
Predict
Not Taken
Taken
Not taken
Not taken
Not taken
Not taken
Taken
Taken
Taken
A 2-bit scheme can give about 80% accuracy
A prediction must be wrong twice before the prediction bit is changed

## Slide 124: 2-bit Predictors
A 2-bit scheme can give about 80% accuracy
A prediction must be wrong twice before the prediction bit is changed
Predict
Taken
Predict
Not Taken
Predict
Taken
Predict
Not Taken
Taken
Not taken
Not taken
Not taken
Not taken
Taken
Taken
Taken
0
1
1
0
BHT also stores the initial FSM state
10
11
01
00

## Slide 125: Branch Target Buffer
The BHT predicts when a branch is taken, but does not tell where it’s taken to!
  A branch target buffer (BTB) in the IF stage can cache the branch target address, but we also need to fetch the next sequential instruction. The prediction bit in IF/ID selects which “next” instruction will be loaded into IF/ID at the next clock edge
    Would need a two read port instruction memory
If the prediction is correct, stalls can be avoided no matter which direction they go
  Or the BTB can cache the branch taken instruction while the instruction memory is fetching the next sequential instruction
Read
Address
Instruction
Memory
PC
0
BTB

## Slide 126: Solution: Branch Target Buffer (BTB)
A cache-like storage that records branch addresses and associated targets (indexed by the instruction address)
  Why tag? – (Hint: desiring 1 cycle BTB lookup)
If there is a hit in BTB for branch predicted taken:
  - PC  Target in BTB for branch
BTB
Target
Tag
Target
Tag
Target
Tag
…
Branch PC
=
=
=
…
0
1
+
4
Branch
Target
Predicted
Branch
Direction

## Slide 127: Challenge: Function Returns
Function returns are frequent, yet
  Address is difficult to compute (have to wait until EX stage done to know it)
  Address is difficult to predict with BTB (function can be called from multiple places)
foo(….)
{
…
0x10001000 jal bar
0x10001004 …
…
0x10001800 jal bar
0x10001804 …
…
0x10001CE4 jal bar
0x10001CE8 …
...
}
bar(….)
{
…
0x1000F0E0 jal baz
0x1000F0E4 …
...
jar $ra
}
baz(….)
{
...
jar $ra
}
But, a return address is in practice simple to predict if it’s aware of ins. semantic
The return address is known from the time of each call!

## Slide 128: Solution: Return Address Stack (RAS)
Call pushes return address into the RAS
When a return instruction decoded, pop the predicted return address from RAS
+
4
Call PC
RET
Push
Return
Address
BTB
Return PC
BTB
Return?
RET

## Slide 129: Solution: Return Address Stack (RAS)
Source: 2003 Elsevier Science (USA). All rights reserved.
Accurate prediction even with small RAS
  8 ~ 16 number of return stack entries is good enough!
MIPS R10K
(1-entry)
DEC Alpha 21164 (#12)
Intel P3 (#16)

## Slide 130: Other Pipeline Structures Are Possible
What about the (slow) multiply operation?
  Make the clock twice as slow or …
  let it take two cycles (since it doesn’t use the DM stage)
ALU
IM
Reg
DM
Reg
MUL
ALU
IM
Reg
DM1
Reg
DM2
What if the data memory access is twice as slow as the instruction memory?
  make the clock twice as slow or …
  let data memory access take two cycles (and keep the same clock rate)

## Slide 131: Summary
All modern-day processors use pipelining for performance (a CPI of 1 and fast a CC)
Pipeline clock rate limited by slowest pipeline stage – so designing a balanced pipeline is important
Must detect and resolve hazards
  Structural hazards – resolved by designing the pipeline correctly
  Data hazards
    Stall (impacts CPI)
    Forward (requires hardware support)
  Control hazards – put the branch decision hardware in as early a stage in the pipeline as possible
    Stall (impacts CPI)
    Delay decision (requires compiler support)
    Static and dynamic prediction (requires hardware support)

## Slide 132: Backup

## Slide 133: The Processor: Datapath & Control
Our implementation is simplified
  memory-reference instructions: ld, sd
  arithmetic-logical instructions: add, sub, and, or
  control flow instructions: beq
Generic implementation
  use the program counter (PC) to supply the instruction address and fetch the instruction from memory (and update the PC)
  decode the instruction (and read registers)
  execute the instruction
All instructions use the ALU after reading the registers
How? memory-reference? arithmetic? control flow?
Fetch
PC = PC+4
Decode
Exec

## Slide 134: Clocking Methodologies
The clocking methodology defines when signals can be read and when they are written
  An edge-triggered methodology
Typical execution
  read contents of state elements
  send values through combinational logic
  write results to one or more state elements
State
element
1
State
element
2
Combinational
logic
clock
one clock cycle
Assume state elements are written on every clock cycle; if not, need explicit write control signal
  write occurs only when both the write control is asserted and the clock edge occurs
Notes: Clocking methodology: 时钟同步方法 -> 军训的时候迈大步
Combinational logic：组合逻辑
State element：状态单元 -> D触发器，寄存器，存储器

## Slide 135: Single Cycle Disadvantages & Advantages
Disadvantages: uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
  especially problematic for more complex instructions like floating point multiply
Disadvantages: may be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
but
Advantages: Is simple and easy to understand
Clk
lw
sw
Waste
Cycle 1
Cycle 2

## Slide 136: Multicycle Datapath Approach
Let an instruction take more than 1 clock cycle to complete
  Break up instructions into steps where each step takes a cycle while trying to
    balance the amount of work to be done in each step
    restrict each cycle to use only one major functional unit
  Not every instruction takes the same number of clock cycles
In addition to faster clock rates, multicycle allows functional units that can be used more than once per instruction as long as they are used on different clock cycles, as a result
  only need one memory – but only one memory access per cycle
  need only one ALU/adder – but only one ALU operation per cycle
Notes: Multiple cycle：多周期

## Slide 137: Multicycle Datapath Approach, con’t
At the end of a cycle
  Store values needed in a later cycle by the current instruction in an internal register (not visible to the programmer). All (except IR) hold data only between a pair of adjacent clock cycles (no write control signal needed)
  IR – Instruction Register MDR – Memory Data Register
  A, B – regfile read data registers ALUout – ALU output register
Address
Read Data
(Instr. or Data)
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
  Data used by subsequent instructions are stored in programmer visible registers (i.e., register file, PC, or memory)

## Slide 138: The Multicycle Datapath with Control Signals
Address
Read Data
(Instr. or Data)
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
Imm
Gen
Shift
left 1
ALU
control
ALUOp
Control
IRWrite
MemtoReg
MemWrite
MemRead
IorD
PCWrite
PCWriteCond
RegDst
RegWrite
ALUSrcA
ALUSrcB
zero
PCSource
1
1
1
1
1
1
0
0
0
0
0
0
2
3
4
Instr[30,14-12]
Instr[]
Instr[31-0]
Instr [6-0]
64
Notes: 合并了instruction memory和data memory
合并了多个ALU的部分
同一个指令需要访问一个部件多次，如何区分？

## Slide 139: Multicycle Control Unit
Multicycle datapath control signals are not determined solely by the bits in the instruction
  e.g., op code bits tell what operation the ALU should be doing, but not what instruction cycle is to be done next
Must use a finite state machine (FSM) for control
  a set of states (current state stored in State Register)
  next state function (determined by current state and the input)
  output function (determined by current state and the input)
Combinational
control logic
State Reg
Inst
Opcode
Datapath
control
points
Next State
. . .
. . .
. . .
Notes: FSM->有限状态机

## Slide 140: The Five Steps of the Load Instruction
IFetch: Instruction Fetch and Update PC
Dec: Instruction Decode, Register Read, Sign Extend Offset
Exec: Execute R-type; Calculate Memory Address; Branch Comparison; Branch Completion
Mem: Memory Read; Memory Write Completion; R-type Completion (RegFile write)
WB: Memory Read Completion (RegFile write)
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
ld
INSTRUCTIONS TAKE FROM 3 - 5 CYCLES!
Notes: Load指令可以根据工作量分为5步：

## Slide 141: Multicycle Advantages & Disadvantages
Advantages: uses the clock cycle efficiently – the clock cycle is timed to accommodate the slowest instruction step
Advantages: multicycle implementations allow functional units to be used more than once per instruction as long as they are used on different clock cycles
but
Disadvantages: requires additional internal state registers, more muxes, and more complicated (FSM) control
Clk
Cycle 1
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type

## Slide 142: Single Cycle vs. Multiple Cycle Timing
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type
Clk
Single Cycle Implementation:
lw
sw
Waste
Cycle 1
Cycle 2
multicycle clock slower than 1/5th of single cycle clock due to state register overhead

## Slide 143: How Can We Make It Even Faster?
Option 1: split the multiple instruction cycle into smaller and smaller steps
  There is a point of diminishing returns where as much time is spent loading the state registers as doing the work
Option 2: start fetching and executing the next instruction before the current one has completed
  Pipelining – (all?) modern processors are pipelined for performance
  Remember the performance equation: CPU time = CPI * CC * IC
Option 3: fetch (and execute) more than one instruction at a time
  Superscalar processing – stay tuned
Notes: Option 1：以前的CPU确实想要增加时钟周期
Option 2：observe that modules are not always busy
需要注意的一点：fetch
CPI: cycle per instruction
CC: clock
IC: instruction count
So we consider introducing pipelining.

## Slide 144: A Pipelined Processor
Start the next instruction before the current one has completed
  improves throughput - total amount of work done in a given time
  instruction latency (execution time, delay time, response time - time from the start of an instruction to its completion) is not reduced
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
ld
Cycle 7
Cycle 6
Cycle 8
sd
IFetch
Dec
Exec
Mem
WB
R-type
IFetch
Dec
Exec
Mem
WB
    clock cycle (pipeline stage time) is limited by the slowest stage
    for some instructions, some stages are wasted cycles

## Slide 145: Single Cycle, Multiple Cycle, vs. Pipeline
Multiple Cycle Implementation:
Clk
Cycle 1
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type
lw
IFetch
Dec
Exec
Mem
WB
Pipeline Implementation:
IFetch
Dec
Exec
Mem
WB
sw
IFetch
Dec
Exec
Mem
WB
R-type
Clk
Single Cycle Implementation:
lw
sw
Waste
Cycle 1
Cycle 2

## Slide 146: Pipeline Datapath Modifications
What do we need to add/modify in our datapath?
  State registers between each pipeline stage to isolate them
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
32
64
ALU
Shift
left 1
Add
Data
Memory
Address
Write Data
Read
Data
IFetch/Dec
Dec/Exec
Exec/Mem
Mem/WB
IF:IFetch
ID:Dec
EX:Execute
MEM:
MemAccess
WB:
WriteBack
System Clock
Imm
Gen
How about control signals
Notes: 流水线的设计跟多周期处理器设计有什么区别？
需要保证不同stage使用的模块都是独立的：instruction memory、data memory、ALU
单个stage内可以看成单周期处理器：譬如branch，需要同时算目标PC地址和比较不同寄存器的值
Chapter 4.6

## Slide 147: Control Signals
Instruction | Execution/address calculation stage control lines |  | Memory access stage control lines |  |  | Write-back stage control lines | 
 | ALUOp | ALUSrc | Branch | Mem- Read | Mem- Write | Reg- Write | Memto- Reg
R-format | 10 | 0 | 0 | 0 | 0 | 1 | 0
ld | 00 | 1 | 0 | 1 | 0 | 1 | 1
sd | 00 | 1 | 0 | 0 | 1 | 0 | X
beq | 01 | 0 | 1 | 0 | 0 | 0 | X

## Slide 148: Pipelining the RISC-V ISA
What makes it easy
  all instructions are the same length (32 bits)
    can fetch in the 1st stage and decode in the 2nd stage
  few instruction formats with carefully designed fields
    can begin reading register file in 2nd stage
  memory operations can occur only in loads and stores
    can use the execute stage to calculate memory addresses
  each instruction writes at most one result (i.e., changes the machine state) and does so near the end of the pipeline (MEM and WB)
What makes it hard
  structural hazards: what if we had only one memory?
  control hazards: what about branches?
  data hazards: what if an instruction’s input operands depend on the output of a previous instruction?
Notes: Hazard：冒险
Structural hazard：结构冒险
Control hazard：控制冒险
Data hazard：数据冒险