## Slide 1: Multi-issue Processor
Jie Zhang
jiez@pku.edu.cn
[Adapted from EE488, Myoungsoo Jung, KAIST]
Notes: 需要加入RAS的解释
需要加入true dependency，anti-dependency和output dependency的解释

## Slide 2: Remind: Performance w/ Pipelining
We finish one instruction per cycle
  After the initial warm-up period
Instruction throughput
  Latch at end of each stage adds latency
  Longest stage determines clock cycle time
  Example:
IF | 1.0 ns
ID | 0.6 ns
EX | 0.9 ns
MEM | 1.2 ns
WB | 0.4 ns
Design | Cycle time | Inst/Cycle
Single cycle |  | 1
Pipeline |  | 1
4.1 ns (sum)
1.2 ns (max)
Speedup due to pipelining: 3.42
Note: ideally it would be 5

## Slide 3: Then, How about using Deeper pipelines?
Goal: Speedup ~ number of stages
Idea: let’s have a lot of stages
  Vaguely defined by deep pipelining
  How about > 30? Think Pentium 4.
What does this mean by?
  While splitting a stage into multiple sub-stages, the machine can issue a new instruction every minor cycle
  If one splits the stage into “m” sub-stages, the clock cycle period “T” should be reduced by “T/m”
Called Super-pipelining
Fetch
Decode
Inst
F1
F2
D1
D2
E1
E2
T
T/m

## Slide 4: Ideal Case of Super-pipelining
The super-pipeline produces the result every T/m clock cycle
Instr. i
Instr. i+1
Pipelining
Super-
Pipelining
Instr. i
Fetch
Decode
Inst
Instr. i+1
Fetch
Decode
Inst
Instr. i+2
Fetch
Decode
Inst
Instr. i+3
Fetch
Decode
Inst
F1
F2
F1
D1
F2
D2
D1
E1
D2
E2
E1
E2
Instr. i+2
F1
F2
D1
D2
E1
E2
Instr. i+3
F1
F2
D1
D2
E1
E2
Cycle1
Cycle2
Cycle3
Cycle4
Cycle5
Gain
T/m

## Slide 5: Problems of Super-pipelining
Require a really high clock frequency!
Instruction dependences (similar to pipelining, but much more critical)
Control dependences
Data dependences
comparison
1
beq
2
1
Instr1
3
2
1
Instr2
5
4
3
2
6
5
4
3
6
5
4
7
6
5
4
3
2
1
Instr3
32
1
Instr31
Result: Branch!
Flush 31 Instr.!
Value from memory arrives
1
LW R1,0(R2)
3
2
5
4
40
ADD R2,R3,R1
1
3
2
25
Value of R1 needed
Stall 15 cycles!
Notes: Data dependences: load/use hazard requires 1 stall in 5-stage pipeling

## Slide 6: There is an Optimal Number of Stages
Source: “Runtime Aware Architectures”, Mateo Valero, HiPEAC CSW 2014
For a given architecture and associated instruction set
Also need to consider workload characteristics
Diminishing Returns: Increasing the number of stages over this limit reduces the overall performance
Around ~15 stages

## Slide 7: Another Instruction-Level Parallelism (ILP)
Internal of operation principle of ILP-processors
Pipelined operation
Parallel operation
EX1
EX2
EX3
Pipelined processors
EX1
EX2
EX3
Instr
Superscalar / VLIW
Orthogonal Design

## Slide 8: Super-scalar
Dynamic multiple-issue processors (decision making at run time by the hardware)
Pentium 4
MIPS R10K
HP PA 8500
IBM Power 3

## Slide 9: Dynamic Multiple Issue Machine (Superscalar)
Superscalar architectures allow several instructions to be issued and completed per clock cycle
A superscalar architecture consists of a number of pipelines that are working in parallel (N-way Superscalar)
  Can issue up to N instructions per cycle
Conceptual N-Way Superscalar
InstructionMemory
Addr
Data
Clock
PC
A1
A2
A3
A4
A5
A6
WD3
WD6
RD1
RD4
RD2
RD5
Register File
ALUs
Data
Memory
WD1
WD2
A1
A2
RD1
RD2
Multi port
Multi port
Multi ALUs
Multi mux
Notes: Assume we have two-way superscalar

## Slide 10: Super-pipelining vs. Super-scalar
Note that super-pipelining is orthogonal with super-scalar
Instr. i
Instr. i+1
Instr. i+2
Instr. i+3
2-way
Super-
scalar
Fetch
Fetch
Decode
Decode
Fetch
Fetch
Inst
Inst
Decode
Decode
Inst
Inst
Super-
Pipelining
Instr. i
Instr. i+1
Instr. i+2
Instr. i+3
F1
F2
F1
D1
F2
F1
D2
D1
F2
F1
E1
D2
D1
F2
E2
E1
D2
D1
E2
E1
D2
E2
E1
E2
Cycle1
Cycle2
Cycle3
Cycle4
Cycle5
Gain
Parallel execution

## Slide 11: Superscalarity is Important!
Ideal case of N-way Super-scalar
  All instructions were independent
  Speedup is “N” (Superscalarity)
Fetch
Fetch
Fetch
Decode
Decode
Decode
Inst
Inst
Inst
What if all instructions are dependent?
  No speed up, super-scalar brings nothing
  (Just similar to pipelining)
Fetch
Fetch
Decode
Fetch
Decode
Inst
Decode
Inst
Inst

## Slide 12: Pipelining vs. Super-scaler
Assembly Code
C Program
Superscalarity ex.: sum of array elements
(assume that load-to-use dependence only take a cycle for the sake of brevity)
sum += a[i--]
loop:
Compile
Pipelining
architecture
Fetch
Decode
ld
Fetch
Decode
add
Fetch
Decode
sub
Fetch
Decode
bne
Superscaler
architecture
Fetch
Decode
ld
Fetch
Decode
add
Fetch
Decode
sub
Fetch
Decode
bne
We should find out independent instructions!
Cannot execute in parallel
Cannot execute in parallel
add $r3, $r3, $r2
ld $r2, 10($r1)
bne $r1, $r0, loop
sub $r1, $r1, 1
Parallel execution
$r2
$r1
$r3
Notes: ld and sub: write after read hazard
sub and bne: read after write hazard

## Slide 13: From Sequential Instructions to Parallel Execution
Q1. How’s the ability of a superscalar processor to execute instructions in parallel determined?
The number and nature of parallel pipelines
The mechanism that the processor uses finds independent instructions (which can be executed in parallel)
The policies used for the instruction execution are characterized by the following factors
 The order in which instructions are issued for execution (In-Order/Out-Order)
 The order in which instructions are completed (In-Order/Out-Order)
Q. BTW, what’s the meaning of controlling instruction completion?
Determine when the instruction write results into registers and memory locations
Notes: How many parallel data paths?
How to identify the independent instructions?

## Slide 14: Execute in Parallel
Execute and complete instructions in their sequential order (but a little chance to execute in parallel)
To improve parallelism, superscalar has to look ahead and try to find independent instructions to execute in parallel
Instructions will be executed in an order different from the strictly sequential one, with the restriction that the result must be correct
   Ideas for the execution policies; we will learn more details with specific techniques for this, partially today and more in future
But Make Sure Sequential Order

## Slide 15: Example Scenario of Parallel Execution Policy
We consider the following instruction sequence:
  I1: ADDF R12,R13,R14 R12 ← R13 + R14 (float. pnt.)
  I2: ADD R1,R8,R9 R1 ← R8 + R9
  I3: MUL R4,R2,R3 R4 ← R2 * R3
  I4: MUL R5,R6,R7 R5 ← R6 * R7
  I5: ADD R10,R5,R7 R10 ← R5 + R7
  I6: ADD R11,R2,R3 R11 ← R2 + R3
Assumption:
  I1 requires two cycles to execute
  I3 and I4 are in conflict for the same functional unit
  I5 depends on the value produced by I4 (we have a true data dependency between I4 and I5);
  I2, I5 and I6 are in conflict for the same functional unit

## Slide 16: Example Scenario of Parallel Execution Policy
Parallel execution policy 1
  Issue: In-Order & Completion: In-Order
  Instructions are issued in the exact order that would correspond to sequential execution; results are written (completion) in the same order
Parallel execution policy 2
  Issue: Out-of-Order & Completion: Out-of-Order
  Out-of-order issue takes the set of decoded instructions the processor looks ahead and issues any instruction, in any order, as long as the program execution is correct

## Slide 17: Example Scenario of Parallel Execution Policy
Parallel execution policy 1
  Issue: In-Order & Completion: In-Order
  Instructions are issued in the exact order that would correspond to sequential execution; results are written (completion) in the same order
Parallel execution policy 2
  Issue: Out-of-Order & Completion: Out-of-Order
  Out-of-order issue takes the set of decoded instructions the processor looks ahead and issues any instruction, in any order, as long as the program execution is correct

## Slide 18: Parallel Execution Policy1
  I1: ADDF $R12, $R13, $R14
  I2: ADD $R1, $R8, $R9
  I3: MUL $R4, $R2, $R3
  I4: MUL $R5, $R6, $R7
  I5: ADD $R10, $R5, $R7
  I6: ADD $R11, $R2, $R3
Considerations
: Two cycle to execute
: I2, I5, I6 same functional unit
: I3, I4 same functional unit
: True data dependency
Cycle
1
2
3
4
5
6
7
8
Decode/Issue
Execute
Writeback/Complete
I1
I2
I3
I4
I5
I6
I1
I1
I5
I6
I2
I3
I4
ADDF
unit
ADD
unit
MUL
unit
An instruction cannot be issued before the previous one has been issued
I1
I2
An instruction completes only after the previous one has completed
I3
I4
I5
I6
In-Order Issue with In-Order Completion
Notes: 我们这没有LD、ST指令，所以就把MEM步骤给取消掉了

## Slide 19: Parallelism Depends on the Program
The processor detects and handles (by stalling) true data dependencies and resource conflicts.
As instructions are issued and completed in their strict order, the resulting parallelism is very much dependent on the way where the program is written/compiled.
  I1: ADDF $R12, $R13, $R14
  I2: ADD $R1, $R8, $R9
  I3: MUL $R4, $R2, $R3
  I4: MUL $R5, $R6, $R7
  I5: ADD $R10, $R5, $R7
  I6: ADD $R11, $R2, $R3
  I1: ADDF $R12, $R13, $R14
  I2: ADD $R1, $R8, $R9
  I6: ADD $R11, $R2, $R3
  I4: MUL $R5, $R6, $R7
  I5: ADD $R10, $R5, $R7
  I3: MUL $R4, $R2, $R3
Switch I3, I6 position
Parallel execution
In-Order Issue with In-Order Completion

## Slide 20: Rewrite Code for Better Parallelism
Considerations
: Two cycle to execute
: I2, I5, I6 same functional unit
: I3, I4 same functional unit
: True data dependency
Cycle
1
2
3
4
5
6
7
8
Decode/Issue
Execute
Writeback/Complete
I1
I2
I6
I4
I5
I3
ADDF
unit
ADD
unit
MUL
unit
I1
I2
  I1: ADDF $R12, $R13, $R14
  I2: ADD $R1, $R8, $R9
  I6: ADD $R11, $R2, $R3
  I4: MUL $R5, $R6, $R7
  I5: ADD $R10, $R5, $R7
  I3: MUL $R4, $R2, $R3
I1
I1
I2
I6
I4
I5
I3
I6
I4
I5
I3
In-Order Issue with In-Order Completion

## Slide 21: Example Scenario of Parallel Execution Policy
Parallel execution policy 1
  Issue: In-Order & Completion: In-Order
  Instructions are issued in the exact order that would correspond to sequential execution; results are written (completion) in the same order
Parallel execution policy 2
  Issue: Out-of-Order & Completion: Out-of-Order
  Out-of-order issue takes the set of decoded instructions the processor looks ahead and issues any instruction, in any order, as long as the program execution is correct

## Slide 22: Parallel Execution Policy2
  I1: ADDF $R12, $R13, $R14
  I2: ADD $R1, $R8, $R9
  I3: MUL $R4, $R2, $R3
  I4: MUL $R5, $R6, $R7
  I5: ADD $R10, $R5, $R7
  I6: ADD $R11, $R2, $R3
Considerations
: Two cycle to execute
: I2, I5, I6 same functional unit
: I3, I4 same functional unit
: True data dependency
Cycle
1
2
3
4
5
6
7
8
Decode/Issue
Execute
Writeback/Complete
I1
I2
I3
I4
I5
I6
I1
I1
I5
I6
I2
I3
I4
ADDF
unit
ADD
unit
MUL
unit
I1
I2
I3
I4
I5
I6
Out-of-Order Issue does not need to wait until I1 is executed
I5
Need to remove true dependency issue!
Similar to Issue, it does not need to wait until I1 is completed
Out-of-Order Issue with Out-of-Order Completion

## Slide 23: Challenges and Considerations of Superscaler
No free lunch! There are dependencies!
Must check dependencies for all instructions, which are
  Simultaneously decoded
  In-progress in the pipeline (e.g., previously issued)
Dependences
(constraints)
Data dependences
Resource dependences
Control dependences
Arise from precedence requirements concerning referenced data
(RAW, WAR, and WAW)
Arise from conditional statements
Arise from limited resources
Naïve solution
(Stalls at decode by comparing)
Rs vs. outstanding targets
Rt vs. outstanding targets + sources
No hardware resources
Stall everything saves these as well, but do we have something better dependencies (this would introduce longer latency)?

## Slide 24: A Set of Better Solutions for Superscalar
  Control dependency
    Loop unrolling of static scheduling
    Branch prediction (learned)
  Dependencies
    Scoreboard
    Static scheduling
    Hardware register renaming of Tomasulo
  Regulation of instruction ordering
    Reservation station
    Reorder buffer/ROB
  Exception handling
To address the dependency issues w/ in-flight instructions

## Slide 25: Superscalar Architecture
Putting all together;
More detailed Superscalar Architecture
Instr$
Fetch &
Addr. Calc. &
Branch pred.
Instr. buffer
Decode & Rename& Dispatch
Instr. Window (queues, reservation stations, etc.)
Instruction issuing
Memory
Floating
Point unit
Integer unit
Integer unit
Commit
Register Files

## Slide 26: Ancient Superscalar Architecture
PowerPC 6XX
  Six independent execution units:
    Branch execution unit
    Load/store unit
    Three integer units
    Floating point unit
  Out-of-order issue
Pentium I/II
  P-I: Three independent units
  P-II: out-of-order, five instructions can be issued in a cycle

## Slide 27: VLIW
Static multiple-issue processors (decision making at compile time by the compiler)
Intel Itanium series for the IA-64 ISA
– EPIC (Explicit Parallel Instruction Computer)

## Slide 28: VLIW: Very Long Instruction Word
Sub-instructions within a long instruction must be independent
Multiple “sub-instructions” can be packed into one long instruction
Each “slot” in a VLIW instruction for a specific functional unit
Key Idea: Replace a traditional sequential ISA with a new ISA that enables the compiler to encode instruction-level parallelism (ILP) directly in the hardware/software interface
C Program
for(i=0;i<n;i++)
dest[i]=
src[i]*coeff;
VLIW Compiler
VLIW Processor
Direct execution
Find independent operations
Schedule
operations
VLIW ISA

## Slide 29: VLIW Hardware (TinyRV1 VLIW Processor)
TinyRV1 VLIW ISA
  No hazard checking, assume ISA enables setting bypass muxing
F
4
D
4
Y0
Y1
Y2
Y3
W
4
X0
L0
L1
S0
S1
4-cycle Y-pipe
, 1-cycle X-pipe
, 2-cycle L-pipe
, 2-cycle S-pipe
mul x1,x2,x3
add x4, x1, x5
lw x6, 0(x7)
sw x6, 0(x8)
VLIW
Instruction
Y-pipe
X-pipe
L-pipe
S-pipe
mul x1,x2,x3
add x4, x1, x5
lw x6, 0(x7)
sw x6, 0(x8)
Y-pipe
X-pipe
L-pipe
S-pipe
mul
add
lw
sw

## Slide 30: VLIW Software (Compilation Techniques)
Key Questions:
  How do we find independent instructions to fetch/execute?
  How to enable more compiler optimizations?
Key Ideas:
  Get rid of control flow
    Predicated execution, loop unrolling
  Optimize frequently executed code-paths
    Trace scheduling
  Others: Software pipelining

## Slide 31: Compile Technique1: Loop Unrolling
Key idea: Unroll loop to perform M iterations at once
Limitations: Code growth, does not handle inter-iteration
  For (i=0; i<N; i++)
  B[i] = A[i] + C;
  For (i=0; i<N; i+=4)
VLIW Compiler
Loop Unrolling…
Original C code
Optimized C code
  {
  }
  B[i] = A[i]+C;
  B[i+1]=A[i+1]+C;
  B[i+2]=A[i+2]+C;
  B[i+3]=A[i+3]+C;
Expose more Instruction-level Parallelism!

## Slide 32: Compile Technique2: Predicated Execution
Key idea: Eliminate hard-to-predict branches by converting control dependence to data dependence
if (cond) {
b = 0;
}
else {
b = 1;
}
Original C code
(normal branch code)
C
B
D
A
T
N
p1 = (cond)
branch p1, TARGET
A
B
C
D
A
(predicated code)
mov b, 1
jmp JOIN
B
TARGET:
mov b, 0
C
A
B
C
p1 = (cond)
(!p1) mov b,1
(p1) mov b,0
Notes: 谓词执行或者判定式执行

## Slide 33: Compile Technique2: Predicated Execution
Credits: MICRO’06 Diverge-Merge Processor (DMP) UT-Austin
Fetch Decode Rename Schedule RegisterRead Execute
A
B
C
D
E
F
Predicated Execution
nop
A
B
A
C
B
A
C
B
D
A
D
C
B
E
A
E
D
C
F
B
A
F
E
D
C
B
A
A
F
B
C
D
E
F
E
D
A
B
C
F
E
A
B
C
D
F
E
D
C
B
A
F
E
D
C
A
B
E
D
C
B
A
F
A
F
B
C
D
E
Key idea: Eliminate hard-to-predict branches by converting control dependence to data dependence
Limitations: Reduces perf. if misprediction cost < benefit
A
Branch Prediction
Pipeline flush!!
E
D
B
F
Fetch Decode Rename Schedule RegisterRead Execute

## Slide 34: Advantages & Disadvantages of VLIW
Advantages
  Simpler hardware (potentially less power hungry)
  Potentially more scalable
    Allow more instr’s per VLIW bundle and add more FUs
Disadvantages
  Programmer/compiler complexity and longer compilation times
    Deep pipelines and long latencies can be confusing (making peak performance elusive)
  Lock step operation, i.e., on hazard all future issues stall until hazard is resolved (hence need for predication)
  Object (binary) code incompatibility
  Needs lots of program memory bandwidth
  Code bloat
    Noops are a waste of program memory space
    Loop unrolling to expose more ILP uses more program memory space

## Slide 35: CISC vs RISC vs SuperScalar vs VLIW
 | CISC | RISC | Superscalar | VLIW
Instr size | variable size | fixed size | fixed size | fixed size (but large)
Instr format | variable format | fixed format | fixed format | fixed format
Registers | few, some special | many GP | GP and rename (RUU) | many, many GP
Memory reference |  |  |  | 
Key Issues | decode complexity | data forwarding, hazards | hardware dependency resolution | (compiler) code scheduling
Instruction flow |  |  |  | 
variable size | fixed size | fixed size | fixed size (but large)
variable format | fixed format | fixed format | fixed format
few, some special | many GP | GP and rename (RUU) | many, many GP
embedded in many instr’s | load/store | load/store | load/store
decode complexity | data forwarding, hazards | hardware dependency resolution | (compiler) code scheduling
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
EX
M
WB
IF
ID
EX
M
WB
EX
M
WB

## Slide 36: Static Scheduling

## Slide 37: Recall: Data-Dependence Stalls
Previously, we tried to reduce the program execution time with
But, there are limits due to data-dependency
Single-issue pipeline (Lecture 3)
Multiple-issue; Superscalar
(Lecture 4)
Load-Use (RAW)
What else?
When no bypassing exists
Long-latency instructions
What else?
Instructions executing in a same cycle shouldn't have RAW/WAR
Limits on WAW

## Slide 38: Solution: Instruction Scheduling
Static Scheduling
Dynamic Scheduling
Compile-time
Run-time
Unscheduled
program
Static
Scheduler
Functional Units
Dynamic
Scheduler
Functional Units
Conservative schedule
High-complexity implementation
Low-complexity implementation
High-quality schedule

## Slide 39: Static Scheduling
Static Scheduling
Dynamic Scheduling
Compile-time
Run-time
Unscheduled
program
Static
Scheduler
Functional Units
Dynamic
Scheduler
Functional Units
Statically schedule inst. from the compiler angle! (for data-dep.)

## Slide 40: What is Compiler?
Compiler translates a program written in a high-level language into an equivalent program in a target language
Source file
ChaseLab.c
void main()
{
printf(“Yay!”); }
Machine code
ChaseLab.exe
11011001
01000100
00010000
10101011
Compiler

## Slide 41: Performance Impacts of Compiler
Source: Intel Corp. 2006 (Itanium® 2 4 CPU)
Compiler optimizations may improve performance significantly
1x
Legacy system
(8 CPUs)
Original source, default options
1.2x
Compiler
Compiler
2.5x
O3 – Enable advanced optimizations
Compiler
4x
Compiler directives, minor source changes
Compiler
10x
Adding OpenMP
Performance can be improved 10x by advanced compiler optimization!

## Slide 42: What is Compiler Optimization?
Execution Time = IC * CPI * CCT
IC: Instruction Count
CPI: Cycles per Instruction
CCT: Clock Cycle Time
The most common requirement is to minimize the time taken to execute a program with the restriction that the result must be correct
Conventional optimization
techniques
Optimization
techniques for ILP
Would be improved with compiler optimizations

## Slide 43: Compiler Optimization = Graph Problem!
The input of optimization process is control flow graph (CFG)
  A directed graph where
    Each node represents a statement
    Edges represent control flow
x:= a+b;
y:= a*b;
while (y>a) {
a:=a+1;
x:=a+b;
}
CFG Generation
x:= a+b
y:= a*b
y>a
a:=a+1
x:=a+b
Loop
CFG variations
With basic blocks
x:= a+b
y:=a*b
y>a
a:=a+1
x:=a+b
Basic blocks: a sequence of instructions w/ no branches into or out of the block

## Slide 44: Simple Loop Example
;branch
;decrement pointer
;store result
;add scalar in F2
;F0=array el.
    for(i=1; i<=1000; i++)
    x[i]=x[i] + s;
Simple loop:
Instruction Instruction Delay in producing result using the result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
Load double Store double 0
Integer op Integer op 0
FP ALU op Branch 1
Branch 1
Our machine specification:
Compilation
w/ a vanilla compiler
    Loop: L.D F0, 0(R1)
    ADD.D F4,F0,F4
    S.D F4 0(R1)
    SUBI R1,R1,#8
    BNEZ R1,R2,Loop
Execute in machine
    1. Loop: LD F0, 0(R1)
    2. Stall
    3. ADDD F4,F0,F4
    4. Stall
    5. Stall
    6. SD F4,0(R1)
    7. SUBI R1,R1,#8
    8. Stall
    9. BNEZ R1,R2,Loop
    10. Stall
10 clocks per iteration (5 stalls) => Can we rewrite the code to minimize stalls?

## Slide 45: Scheduled Loop Body (with CFG)
Clock Cycle
    LD F0,0(R1)
    ADDD F4,F0,F2
    SD F4,0(R1)
    SUBI R1,R1,#8
    BNEZ R1,R2,Loop
Compiler optimization
Clock Cycle
    LD F0,0(R1)
    ADDD F4,F0,F2
    SD F4,0(R1)
    BNEZ R1,R2,Loop
    SUBI R1,R1,#8
5 stalls  1 stalls!
8
Utilize delayed
branch slot
Notes: To schedule the delayed branch, the compiler had to determine that it could swap the SUBI and SD by changing the address to which the SD stored: 0(R1) is replaced with 8(R1). It is not a trivial observation, since most compilers would see that SD depends on SUBI and would refuse to interchange them. However, the smarter compilers could figure out the relationship and performs the interchange.

## Slide 46: Goal of Multi-Issue Scheduling
Place as many independent instructions in sequence
  “as many”  up to execution bandwidth
    Don’t need 7 independent instructions on a 3-wide machine
  Avoid pipeline stalls
If compiler is really good, we should be able to get high performance on an in-order superscalar processor
  In-order superscalar provides execution bandwidth, compiler provides dependence scheduling

## Slide 47: Why this Should work?
Execution
window
Software window
Compiler has “all the time in the world” to analyze instructions
  Hardware must do it in < 1ns
Compiler can “see” a lot more
  Compiler can do complex inter-procedural analysis, understand high-level behavior of code and programming language
  Hardware can only see a small number of instructions at a time
Static detection & resolution of dependencies (Compiler)
Dynamic detection & resolution of dependencies (HW)
Input code
ILP
compiler
Issue
window
Input code
Instruction issue unit of the processor

## Slide 48: Why might this not work?
Can’t always schedule around branches
  limited access to dynamic information (profile-based info)
  Perhaps none at all, or not representative
  Ex. Branch T in 1st ½ of program, NT in 2nd ½, looks like 50-50 branch in profile
Not all stalls are predicable
  Cannot react to dynamic events like data cache misses
Although there are limits of static scheduling (done by compiler), there is still a room to reap the benefits.
Let’s check the detail techniques!

## Slide 49: Conventional Optimization Techniques
Execution Time = IC * CPI * CCT
IC: Instruction Count
CPI: Cycles per Instruction
CCT: Clock Cycle Time
We mainly focus on Instruction Count!

## Slide 50: Technique1: Register Renaming
Observation1: weird register allocation
  Largely limited by architected registers
  Could possibly cause more spills/fills
Observation2: Dynamic Dead Code (branches)
  Code motion may be limited
    R5=R1-R4
    R1=LOAD 0[R6]
    R1=R2+R3
    BEQZ R9
R8
R8
Need to allocate registers differently
Causes unnecessary execution of LOAD when branch goes left
Notes: Reduced Dead Code: Register renaming can lead to the elimination of some dynamic dead code. When a register is renamed, the processor can track whether the original register's value is needed anymore. If not, the instructions that compute this value can be regarded as dead code and can be removed or ignored.

## Slide 51: Register Renaming & Scheduling
A: R1 = R2 + R3
B: R4 = R1 – R5
C: R1 = LOAD 0[R7]
D: R2 = R1 + R6
E: R6 = R3 + R5
F: R5 = R6 – R4
No need to same
No need to same
A: R1 = R2 + R3
B: R4 = R1 – R5
C’: R8 = LOAD 0[R7]
D’: R2 = R8 + R6
E’: R9 = R3 + R5
F’: R5 = R9 – R4
Renaming
Schedule to remove stall
A: R1 = R2 + R3
C’: R8 = LOAD 0[R7]
B: R4 = R1 – R5
E’: R9 = R3 + R5
D’: R2 = R8 + R6
F’: R5 = R9 – R4
Same functionality, no stalls
A
B
C
D
E
F
A
B
C
D
E
F
A
C’
B
E’
F
D’
CFG view
Renaming
Scheduling

## Slide 52: Technique2: Loop Unrolling
Transforms an M-iterations loop into a loop with M/N iterations
  We say that the loop has been unrolled N times
Some compilers can do this (gcc –funroll-loops) or you can do it manually (above)
for(i=0;i<100;i+=4){
a[i]*=2;
a[i+1]*=2;
a[i+2]*=2;
a[i+3]*=2;
}
for(i=0;i<100;i++)
a[i]*=2;

## Slide 53: Why Loop Unrolling? (1)
Get rid of small loops
for(i=0;i<4;i++)
a[i]*=2;
a[0]*=2;
a[1]*=2;
a[2]*=2;
a[3]*=2;
Easier: no branches in the way
for(0)
for(1)
for(2)
for(3)
Difficult to schedule/hoist
insts from bottom block to
top block due to branches

## Slide 54: Why Loop Unrolling? (2)
Less loop overhead
Allow better scheduling of instructions
L.D F0,0(R1)
ADD.D F0,F0,F2
S.D F0,0(R1)
DADDUI R1,R1,#-8
BNE R1, R2, Loop
L.D F0,0(R1)
ADD.D F0,F0,F2
S.D F0,0(R1)
DADDUI R1,R1,#-8
BNE R1, R2, Loop
L.D F0,0(R1)
ADD.D F0,F0,F2
S.D F0,0(R1)
DADDUI R1,R1,#-8
BNE R1, R2, Loop
Unroll
4 branches -> 1 branches
L.D F0,0(R1)
ADD.D F0,F0,F2
S.D F0,0(R1)
L.D F0,-8(R1)
ADD.D F0,F0,F2
S.D F0,-8(R1)
L.D F0,-16(R1)
ADD.D F0,F0,F2
S.D F0,-16(R1)
L.D F0,-24(R1)
ADD.D F0,F0,F2
S.D F0,-24(R1)
DADDUI R1,R1,#-32
BNE R1, R2, Loop
L.D F0,0(R1)
ADD.D F0,F0,F2
S.D F0,0(R1)
DADDUI R1,R1,#-8
BNE R1, R2, Loop

## Slide 55: Loop Unrolling: Problems
Program size becomes larger (code bloat)
Q1. What if N is not a multiple of M?
Q2. Or What if N is unknown at compiler time?
Q3. Or What if it is a while loop?
j1=j-j%4;
for(i=0;i<j1;i+=4){
a[i]*=2;
a[i+1]*=2;
a[i+2]*=2;
a[i+3]*=2;
}
for(i=j1;i<j;i++)
a[i]*=2;
for(i=0;i<j;i++)
a[i]*=2;
Unroll until value`i` is multiple of 4
Remained for another for loop

## Slide 56: Technique3: Function Inlining
Goal: sort of like “unrolling” a function
Problems: primarily code bloat
Normal Function
Start
Stop
myfunc();
myfunc()
{
// body
}
call
return
Inline Function
Start
Stop
Main function body
{
}
myfunc()
{
// body
}
myfunc()
Remove function call overhead
  CALL/RETN (and possible branch misprds)
  Argument/ret-val passing, stack allocation, and associated spills/fills of caller/calle-save regs
Larger block of instructions for scheduling

## Slide 57: Technique4: Tree Height Reduction
Goal: shorten critical path(s) using associativity law
Limitations: not all math operations are associative!
C defines L-to-R semantics for most arithmetic
R8=((R2+R3)+R4)+R5
I1:ADD R6,R2,R3
I2: ADD R7,R6,R4
I3: ADD R8,R7,R5
I1
I2
I3
R8=(R2+R3)+(R4+R5)
Associativity
ADD R6,R2,R3
ADD R7,R4,R5
ADD R8,R7,R6
I1
I2
I3

## Slide 58: Optimization Techniques for ILP
Execution Time = IC * CPI * CCT
IC: Instruction Count
CPI: Cycles per Instruction
CCT: Clock Cycle Time
We mainly focus on Cycles/Instruction!

## Slide 59: Scheduling for Inst-Level Parallelism
Goal: Schedule instructions to finish whole program as soon as possible
Two types of static ILP scheduling
Global Scheduling
Software Pipelining
Static ILP Scheduling
Target: DAG (Directed Acyclic Graph) of a general purpose integer program with many conditional branches
Target: loop in any code

## Slide 60: Technique1: Global Scheduling
 No good enough # of instructions which can be processed in parallel
Q. What is the general size of basic block?
In general, the basic block size of non-numeric computation program is 5~20 instructions
x:= a+b
y:=a*b
y>a
a:=a+1
x:=a+b
[REMIND] Basic blocks: a sequence of instructions w/ no branches into or out of the block
Q. Why global scheduling?
As the basic block size is too small to find out independent instructions, let’s schedule the instructions that exist across all other basic blocks (e.g., in global)
Trace-based Scheduling
DAG-based schdeuling
Global Scheduling
Will be covered
In this lecture

## Slide 61: Trace-based Scheduling
This is one technique for global scheduling
  Works on all code, not just loops
  Take an execution trace of the common case
  Schedule code as if it had no branches
  Check branch condition when convenient
  If mispredicted, clean up the mess
Q. How do we find the “common case”
A. Program analysis or profiling

## Slide 62: Example of Trace Scheduling
a=log(x);
if(b>0.01){
c=a/b;
}else{
c=0;
}
y=sin(c);
a=log(x);
c=a/b;
y=sin(c);
if(b<=0.01)
goto fixit;
fixit: c=0;
y=0; // sin(0)
Suppose profile says that b>0.01 90% of the time
Now, we have a larger basic block for the trace scheduling & optimizations
90%
10%
90%
10%

## Slide 63: Pay Attention to Cost of Fixing
Assume the code for b > 0.01 accounts for 80% of the time
Optimized trace runs 15% faster
But, fix-up code may cause the remaining 20% of the time to be even slower!
Assume fixup code is 30% slower
[REMIND] Amdahl’s law
= System performance
P: Fraction of enhanced component
S: Speedup of enhanced component
11.7%
4.6%
Around 2/3 of the benefit removed

## Slide 64: Technique2: Software Pipelining
Design: overlapping different iterations by starting the next iteration before the current iteration in the loop ends
Consider a graphical view of the overlay of iterations:
Epilog
Kernel
Prolog
Only the shaded part, the loop kernel, involves executing the full width of the VLIW instruction.
  The loop prolog and epilog contain only a subset of the instructions.
    “ramp up” and “ramp down” of the parallelism.
Inst1
Inst2
Inst3
Inst4
Inst1
Inst2
Inst3
Inst4
Inst1
Inst2
Inst3
Inst4
interation1
interation2
interation3
interation4
interation5
interation6

## Slide 65: Scheduling Loop Unrolled Code
Schedule
Int1
Int 2
M1
M2
FP+
FPx
loop:
loop: ld f1, 0(r1)
ld f2, 8(r1)
ld f3, 16(r1)
ld f4, 24(r1)
add r1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
sd f5, 0(r2)
sd f6, 8(r2)
sd f7, 16(r2)
sd f8, 24(r2)
add r2, 32
bne r1, r3, loop
Unroll 4 ways
ld f1
ld f2
ld f3
ld f4
add r1
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r2
bne
Assumption:
ld: 2 cycle
Assumption:
fadd: 3 cycle

## Slide 66: Software Pipelining
Schedule
loop: ld f1, 0(r1)
ld f2, 8(r1)
ld f3, 16(r1)
ld f4, 24(r1)
add r1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
sd f5, 0(r2)
sd f6, 8(r2)
sd f7, 16(r2)
sd f8, 24(r2)
add r2, 32
bne r1, r3, loop
Unroll 4 ways first
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r1
add r2
bne
Int1
Int 2
M1
M2
FP+
FPx
loop:
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r1
add r2
bne
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5

## Slide 67: Loop Unrolling vs. Software Pipelining
time
performance
Loop Iteration
Software pipelining pays startup/wind-down costs only once per loop, not once per iteration
Loop Unrolling
Software Pipelining
Startup overhead
Wind-down overhead
performance
time
Loop Iteration

## Slide 68: Recall: Why Compiler Might not Work
Can’t always schedule around branches
  limited access to dynamic information (profile-based info)
  Perhaps none at all, or not representative
  Ex. Branch T in 1st ½ of program, NT in 2nd ½, looks like 50-50 branch in profile
Not all stalls are predicable
  Cannot react to dynamic events like data cache misses